TSC / Application Programming Interface

Software API

IOxOS Technologies SA / 4, Chemin des Fontenailles / CH-1196 Gland / SWITZERLAND

IOxOS Technologies SA universal property / The content of this document is the property of IOxOS Technologies SA. It is supplied in confidence and commercial security on its contents must be maintained. It must not be used for any purpose other than that for which it is supplied nor may information contained in it be disclosed to un-authorized persons. It must not be reproduced in whole or part without permission in writing from IOxOS Technologies SA.

Version Control
Version	Date	Chapter and section modifications	Author	Checked	Approved
0.0.1	29 Oct 2015	Initial version (preliminary)	JFG	IGA	JBO
0.0.02	21 No 2017	Update documentation for IC1211 – IFC14xx boards	XP

Author references
Initial	Name	Company	Comments
[JBO]	Joel BOVIER	IOxOS Technologies SA
[JFG]	Jean-Francois GILOT	IOxOS Technologies SA
[IGA]	Iván GARCÍA-ALFONSO	IOxOS Technologies SA
[XP]	Xavier PAILLARD	IOxOS Technologies SA

# Introduction
## Purpose
This manual is intended for use by system designers, software developers and support personnel.
It is recommended that the reader has a reasonable background in PC architectures, including experience or knowledge of I/O buses and related protocols.
## Document Organization
This manual is composed of the following sections
    1. Introduction
    2. Overview
    3. User Library
Section 2 gives an overview of the software architecture
Section 3 is a reference for the programming interface (API)

## Acronyms and Abbreviations
Acronym	Definition
DMA	Direct Memory Access
IO	Input/Output
PC	Personal Computer
PCI	Peripheral Component Interconnect
PCIe	PCI Express

Table 1.1: Acronyms

## References

Reference	Title	Version	Date	Owner
	PCI Local Bus Specification	3.0	Aug 12,2002	PCI-SIG
	PCIe Base Specification	2.0	Jan 4, 2007	PCI-SIG

Table 1.2: References

# Overview
## Software organization
The core of the TSC bridge software is the kernel module “tscklib.c” implementing all functions needed to handle the TSC device:
CSR registers access
- local resources initialization
- device control operations
These function are designed to be exported in order to be used by other modules in the kernel such higher level device drivers.
The first argument of the exported functions is always a pointer to the tsc data structure holding all information need to drive the TSC device.
Critical accesses to the hardware resources are protected by mutexes.
In order to make the source code easily maintainable a set of low level libraries associated to each subsystem are provided to be linked with the kernel modules. Each low level library is associated to a “.h” file in which the implemented functions are declared together with a data structure holding information needed to control the subsystem.
An user library “tsculib.c” is provided to offer an API for the control of the TSC device.
A monitoring/exerciser “TscMon” application linked with the user library offers a set of interactive commands to allow the user to control the TSC device.
### Linux Implementation
The TSC software for Linux is delivered on a compressed archive file labeled TSC_xx.yy.zz.tgz containing all delivered files including the documentation.
The TSC_xx.yy.zz.tgz can be extracted anywhere in the Linux file system and produces a directory tree labeled TSC/ . All sources code are written in C language and has been compiled with the gnu compiler.

The core of the software organization is the TSC device driver. This is a Linux loadable module located in the drivers/ directory of the TSC/ directory tree.
## TSC Kernel Library
As a general rule, all exported functions defined in “tscklib.c” are labeled “tsc_xxx_yyy()” where “xxx” refer to the subsystem and “yyy” to the operation to be performed.
### Device Initialization
The tsc_dev_init() shall be executed at module installation time. It create a protection mutex for TSC registers accesses and call the subsystem initialization functions:
- Interrupt mechanism
- Resource mapping mechanism
- SHM accesses
- Read/write accesses mechanism
- Sflash accesses
- DMA mechanism
- I2c accesses
Before removing the core module, the function tsc_dev_exit() shall be executed to return to the operating system all allocated resources.
### Accessing TSC Registers
The tsc_csr_op() function allows to perform a set of operation on the TSC registers:
- CSR registers
- ARTIX7 SMON registers
- ARTIX7 PCIEP DRP registers
- ARTIX7 PCIEP CFG registers
The “csr_lock” mutex in the tsc_device control structure is used to protect register access.
For ARTIX7 SMON and PCIEP registers, read and write operation are supported.
For TSC CSR registers, the following operations are supported:
- Read, read with mask
- Write, Write with mask
- OR, OR with mask
- XOR, XOR with mask
- AND, AND with mask
For “masked” operation, the operation is performed only for the bit matching the mask parameter. Bit set to 0 in the mask are left untouched.
int
tsc_csr_op( struct tsc_device *tsc,
     struct tsc_ioctl_csr_op *csr_op);

The tsc_ioctl_csr_op data structure defines the operation the be performed. That structure is declared in the “tscioctl.h” file and is shared with the API.
struct tsc_ioctl_csr_op
{
  int operation; /* operation to be performed */
  int offset; /* register offset */
  int data; /* data */
  int mask; /* only for masked operations */
};

This file contains also the definitions of the operation codes:

tsc_IOCTL_CSR_RD → Read register
tsc_IOCTL_CSR_RDm → Read register with mask
tsc_IOCTL_CSR_WR → Write register
tsc_IOCTL_CSR_WRm → Write register with mask
tsc_IOCTL_CSR_OR → OR register
tsc_IOCTL_CSR_ORm → OR register with mask
tsc_IOCTL_CSR_AND → AND register
tsc_IOCTL_CSR_ANDm → AND register with mask
tsc_IOCTL_CSR_XOR → XOR register
tsc_IOCTL_CSR_XORm → XOR register with mask
tsc_IOCTL_CSR_SMON_RD → Read SMON register
tsc_IOCTL_CSR_SMON_WR → Write SMON register
tsc_IOCTL_CSR_PCIEP_RD → Read PCIe End Point register
tsc_IOCTL_CSR_PCIEP_WR → Write PCIe End point

### Managing Remote Resources
The TSC bridge allows to access remote resources such Shared Memory (SHM) from the PCI tree. To perform read/write access to this resources from the PCI tree, a translation window mapping the PCI address to the remote address shall have been prepared. The tsc_map_mas_alloc() function allows to create an address mapping in the master mapper implemented in the TSC device.
The tsc_map_mas_modify() allows to modify an existing mapping and tsc_map_mas_free() to release it.
The tsc_map_mas_get() shall be used to retrieve the mapping parameters such the PCI address to be used to cross the translation window.
The tsc_ioctl_map_win data structure is used to exchange parameters between the client and the mapping functions. That structure is declared in the “tscioctl.h” file and is shared with the API.

struct tsc_ioctl_map_win
{
  int offset;
  union
  {
    struct tsc_ioctl_map_req req;
    struct tsc_ioctl_map_sts sts;
  };
};

The offset field is set by the mapper at allocation time and used by the mapping functions as window identifier. It shall be left untouched by applications.
The tsc_ioctl_map_req and tsc_ioctl_map_sts are two mirror data structures used to hold mapping request and mapping status parameters.
#### Mapping a Resource from PCI
int
tsc_map_mas_alloc( struct tsc_device *tsc,
        struct tsc_ioctl_map_win *w);

When calling tsc_map_mas_alloc(), the tsc_ioctl_map_win data structure shall contain the mapping parameters of the requested window.

struct tsc_ioctl_map_mode
{
  char sg_id; char flags; short hw;
  char ads; char space; char swap; char am;
};

struct tsc_ioctl_map_req
{
  ulong rem_addr;
  ulong loc_addr;
  uint size;
  struct tsc_ioctl_map_mode mode;
};

struct tsc_ioctl_map_sts
{
  ulong rem_base;
  ulong loc_base;
  uint size;
  struct tsc_ioctl_map_mode mode;
};

struct tsc_ioctl_map_win
{
  int pg_idx;
  union
  {
    struct tsc_ioctl_map_req req;
    struct tsc_ioctl_map_sts sts;
  };
};

The tsc_ioctl_map_req data structure is used to provide parameters to the window allocator. The rem_addr field shall be loaded with the address of the remote resource to be mapped.
The loc_addr is updated by the mapper with the PCI address to be used to access the requested rem_addr.
The size field shall be loaded with the request mapping size.
The mode field is a data structure defining the addressing parameters to be used to access the remote resource:
The sg_id field defines which mapper shall be used to access the remote resource. For master access two mappers are available:
MAP_ID_MAS_PCIE_PMEM → PCI PMEM mapper (through PCI BAR #0)
MAP_ID_MAS_PCIE_PEM → PCI MEM mapper (through PCI BAR #2)

The space field defines on which bus the remote resource is hosted:
MAP_SPACE_SHM1 → resource hosted in Shared Memory 1
MAP_SPACE_SHM2 → resource hosted in Shared Memory 2

The swap field defines hardware data swapping mode to be selected:
MAP_SWAP_NO → no swapping
MAP_SWAP_AUTO → auto swap according to data size
MAP_SWAP_DW → double word swapping
MAP_SWAP_QW → quad word swapping

The flags field is not used for master mapping.
The pg_idx field is updated by the mapper and contains the index in the mapping table of the page used for the address translation. That information is used as input parameter by the tsc_map_mas_free() and tsc_map_mas_modify() functions.
#### Getting Parameters of an Allocated Window
The function tsc_map_mas_get() the current parameters of a previously allocated window:
int
tsc_map_mas_get( struct tsc_device *tsc,
        struct tsc_ioctl_map_win *w);

The function expect a pointer the a tsc_ioctl_map_win data structure as second argument to retrieve the mapping parameters.
The pg_idx parameters shall contain the value returned by the allocation function when the window was created.
When calling tsc_map_mas_get() the mapper loads the tsc_ioctl_map_sts data structure with the parameters of the translation window identified by the field offset.
Before calling tsc_map_mas_get(), it is important to set the sg_id field in the tsc_ioctl_map_mode data structure shall be set to identify the targeted mapper.
When tsc_map_mas_get() returns, loc_base is updated with the PCI base address of the translation window and size with the size in bytes of that window.
rem_base and mode are updated with the remote address pointed by loc_base and the access mode parameter.
The function returns the offset.
#### Freeing an Allocated Window
To free an allocated window ,the tsc_map_mas_free() function must be executed:
int
tsc_map_mas_free( struct tsc_device *tsc,
       int sg_id,
       uint pg_idx);

That function needs the mapper sg_id and the pg_idx returned by the allocation function.
#### Modifying an Allocated Window
When a translation window has been allocated, it is possible to modify its mapping parameter with the tsc_map_mas_modify() function:
ulong
tsc_map_mas_modify( struct tsc_device *tsc,
        struct tsc_ioctl_map_win *w);

which takes the same parameters as tsc_map_mas_alloc(). However in this case pg_idx is an input parameters identifying the translation window to be modified.
size and loc_addr are output parameter set to the actual size and base address of that window.
rem_addr and mode parameters shall be loaded with the requested remote address and access mode. In the tsc_ioctl_map_mode data structure the sg_id field shall target the requested mapper.
### Accessing remote resources
During the initialization phase a 64 KByte address translation window in the PCI MEM space is allocated to access dynamically remote resources. The function tsc_rem_read()/tsc_rem_write() allow to transfer data to/from a remote resource using that predefined translation window:
int
tsc_rem_read( struct tsc_device *tsc,
        struct tsc_ioctl_rdwr *rw);

int
tsc_rem_write( struct tsc_device *tsc,
        struct tsc_ioctl_rdwr *rw);

When the read/write functions are called, the remote parameters (address and mode) of that window are set to point on the selected remote resource.
A data structure tsc_ioctl_rdwr is used to pass transfer parameters to the read/write functions:

struct tsc_ioctl_rdwr
{
  ulong rem_addr;
  char *buf;
  int len;
  union
  {
    int mode;
    struct rdwr_mode {char ads; char space; char swap; char am;}m;
  };

The rem_addr field is the address in the remote space where the data have to be read/written. That value, together with mode parameters are passed to the tsc_map_mas_modify() function to create the local address needed to perform the data transfer.
#### Getting Parameters of an Allocated Window
The function tsc_map_mas_get() the current parameters of a previously allocated window:
int
tsc_map_mas_get( struct tsc_device *tsc,
        struct tsc_ioctl_map_win *w);

The function expect a pointer the a tsc_ioctl_map_win data structure as second argument to retrieve the mapping parameters.
The pg_idx parameter shall contain the value returned by the allocation function when the window was created.
When calling tsc_map_mas_get() the mapper loads the tsc_ioctl_map_sts data structure with the parameters of the translation window identified by the field pg_idx.
struct tsc_ioctl_map_sts
{
  ulong rem_base;
  ulong loc_base;
  uint size;
  struct tsc_ioctl_map_mode m;
};

Before calling tsc_map_mas_get(), it is important to set the sg_id field in the tsc_ioctl_map_mode data structure shall be set to identify the targeted mapper.
When tsc_map_mas_get() returns, loc_base is updated with the base address of the translation window and size with the size in bytes of that window.
rem_base and mode are updated with the remote address pointed by loc_base and the access mode parameter.
#### Freeing an Allocated Window
To free an allocated window the tsc_map_mas_free() function shall be executed:

int
tsc_map_mas_free( struct tsc_device *tsc,
      int sg_id,
       uint offset);

That function needs the mapper sg_id and the offset returned by the allocation function.
### Interrupt Handling
TSC implements 64 interrupt sources. For each of these source the kernel library allows to associate a user defined interrupt handler.
It installation time, the tsc_irq_init() function mask all interrupt sources and register the tsc_irq_spurious() handler for each source.
Before calling the user handler, the interrupt source is masked by the tsc_irq() main handler and this is the user's responsibility to unmask it.
After the user's handler returns, interrupt scanning is restarted.
#### Registering an Interrupt Handler
The tsc_irq_register() function shall be called to register a user's handler:
int
tsc_irq_register( struct tsc_device *tsc,
       int src,
       void (* func)( struct tsc_device*, int, void *),
       void *arg)

If a user handler is already registered for the source identified by src the call returns -EBUSY and the registering fails.
The third argument func is the handler address and the fourth argument arg is a user defined pointer passed as argument when the user handler is executed.
To install another user's handler the tsc_irq_unregister() shall be executed first. After that call, the tsc_irq_spurious() is associated to src:
void
tsc_irq_unregister( struct tsc_device *tsc,
        int src)

One can check if a source is associated to a handler by calling the tsc_irq_check_busy() function:
int
tsc_irq_check_busy( struct tsc_device *tsc,
        int src)

#### Masking/Unmasking Interrupt Sources
In order to enable or disable one of the 64 interrupt source, the function tsc_irq_mask() shall be executed:
int
tsc_irq_mask( struct tsc_device *tsc,
        int op,
        int src)

The op parameter defines the operation to be performed, tsc_IOCTL_ITC_MSK_CLEAR to enable the interrupt source identified by src and tscSE_IOCTL_ITC_MSK_SET to disable it.
tsc_IOCTL_ITC_MSK_CLEAR	→ enable interrupt source (clear masking)
tsc_IOCTL_ITC_MSK_SET	→ disable interrupt source (set masking)

## Linux Drivers
### TSC Control Driver
#### Overview
The TSC Control driver tsc.ko is a Linux kernel object containing the TSC kernel library and an interface with the operating system to perform the device initialization (at install time) and to allow application to perform control operations (through ioctl() system calls). The user's library (§TSC User Library) rely on the presence of that driver.
This driver creates (at install time) a device to allows applications to map a portion of the memory address space in order to control various resources (Shared memory, User space).
The ioctl() system call allows to set/get the remote mapping parameters. Once this has been done, the read(), write() system calls can be used to transfer data from/to the memory resources. The mmap() system call is supported to allow transparent access to the memory space from an application.
#### Driver Installation
The Makefile in the driver directory produces a kernel object “tsc.ko” which implement the TSC driver.
insmod tsc.ko #Install the TSC driver

#### Open/Close a Device and execute read / write
The first time a master device is opened, data structures for master mapping and interrupt handling are created. The next example is the codes source of a simple access in user space of a remote resource (Shared memory).

#include <stdlib.h>
#include <stdio.h>
#include <pty.h>
#include <unistd.h>
#include <sys/types.h>
#include <sys/stat.h>
#include <fcntl.h>
#include <string.h>
#include <sys/mman.h>
#include "../../include/tscioctl.h"
#include "../../include/tsculib.h"

main(int argc, char *argv[]){
struct tsc_ioctl_map_win map_win;
int retval = 0;
unsigned int *buf_ddr = NULL;	// Buffer mapped directly in DDR3 area
     unsigned int fd = 0;

// Init TSC
fd = tsc_init();

// Map DDR3 memory region --
buf_ddr = NULL;

// Fill mapping structure
memset(&map_win, sizeof(map_win), 0);
map_win.req.rem_addr = 0x100000;	// Address in SHM1
map_win.req.loc_addr = 0;	// Local address
map_win.req.size = 0x40;	// Mapping size
map_win.req.mode.sg_id = MAP_ID_MAS_PCIE_MEM;	// Memory space
map_win.req.mode.space = MAP_SPACE_SHM1;	// SHM #1
map_win.req.mode.flags = 0;

// Allocate a mapping
retval = tsc_map_alloc(&map_win);
if(retval < 0){
printf("Error in mapping SHM1 \n");
}

// Map in user space resource
buf_ddr = mmap(NULL, map_win.req.size, PROT_READ | PROT_WRITE, MAP_SHARED, fd,	map_win.req.loc_addr);
if(buf_ddr == MAP_FAILED){
printf("Error MAP FAILED \n");
}

// Write / read SHM1 (DDR3 memory)
*buf_ddr = 0xdeadface;
printf("Word written : %x \n", buf_ddr[0]);

// TSC exit
tsc_exit();
}

# TSC User Library
The user library interfaces applications with the TSC device driver. Basically the library functions re-package user's parameters in a data structure ready to be passed to the driver ioctl() functions. If not otherwise stated, library functions returns the value returned by the corresponding ioctl() call. The generic error code for functions returning an integer is -1 (operation not permitted). For function returning a pointer it is the NULL pointer.
## Initialization
To be allowed to call functions defined in libtsc.a, the application shall first call an initialization function performing the open of the driver and initializing the library private data structure.
If that function has not been executed all other functions in the library return the bad file descriptor error code [-9].
It is possible to set the device if the driver drives multiple device.
Prototype

#include <tsculib.h>

int
tsc_init()

Description
That function must be called by the application before invoking any other function belonging to the TSC user's library.
Operations performed by that call are operating system dependent

Linux Implementation:
Among other things, it performs an open of the /dev/bus/bridge/tsc_ctl device and returns the Linux file descriptor. The device node is generated automatically when TSC device driver is installed by Linux.

Parameters
none

Return
fd	tsc_ctl file descriptor (returned by the open call)

Prototype
int
tsc_exit()

Description
Close a tsc_ctl node previously open by tsc_init().

Parameters
none

Return
0	if OK
< 0	if tsc_ctl node was not open

Prototype
int
set_device(int device)

Description
Select the device according to their number.
0 → CENTRAL device
1 → IO device (only on specific board)

Parameters
device	Select the device

Return
0	if OK
< 0	if tsc_ctl node was not open

## Identification

Prototype
char *
tsc_get_drv_name( void)

Description
Returns a pointer to the TSC driver identifier string.

Parameters
none

Return
pointer to driver identifier string

Prototype
char *
tsc_get_drv_version( void)

Description
Returns a pointer to a string holding the driver version.

Parameters
none

Return
pointer to a string holding the driver version.

Prototype
char *
tsc_get_lib_version( void)

Description
Returns a pointer to the a string holding the library version.

Parameters
none

Return
pointer to a string holding the library version.

Prototype
int
tsc_get_device( void)

Description
Return device id either 0 for CENTRAL, 1 for IO.

Parameters
none

Return
Return device id.

Prototype
int
tsc_get_device_id( void)

Description
Return device id.

Parameters
none

Return
Return device id.

Prototype
int
tsc_get_vendor_id( void)

Description
Return vendor id.

Parameters
none

Return
Return vendor id.

## Byte Swapping
Three functions are provided to perform byte swapping of 64, 32 and 16 bit integers.

Prototype
long long
tsc_swap_64( long long data)

Description
Byte swap 64 bit integer.

Parameters
data	64 bit integer to be swapped

Return
swapped data.

Prototype
int
tsc_swap_32( int data)

Description
Byte swap 32 bit integer.

Parameters
data	32 bit integer to be swapped

Return
swapped data.

Prototype
short
tsc_swap_16( short data)

Description
Byte swap 16 bit integer.

Parameters
data	16 bit integer to be swapped

Return
swapped data.

## Register Access
A set of functions allows applications to perform read and write access on the TSC control and status registers (32 bit) mapped in the 4KBytes PCI MEM window (through BAR3).
### TSC CSR Access
#### CSR Read
Prototype

#include <tsculib.h>

int
tsc_csr_read( int idx,
      int *data_p)

Description
Perform a 32 bit read cycle in the TSC PCI MEM space in order to return the current value of the control and status register whose offset is equal to bit 0:12 of the idx parameter.

Parameters
idx	register index (address offset in PCI MEM window)
data_p pointer to a 32 bit integer to hold register content

Return
status of the read operation
< 0 if error

#### CSR Write
Prototype

#include <tsculib.h>

int
tsc_csr_write( int idx,
        int *data_p);

Description
Perform a 32 bit write cycle in the TSC PCI MEM space in order to set the current value of the control and status register whose offset is equal to the idx parameter.

Parameters
idx	register index (address offset in PCI MEM window)
data_p	pointer to a 32 bit integer holding the value to be written

Return
Status of the write operation
< 0 if error

#### CSR Set
Prototype

#include <tsculib.h>

int
tsc_csr_set( int idx,
        int *data_p);

Description
Perform a 32 bit read cycle followed by a 32 bit write cycle in the TSC PCI MEM space in order to set the value of the control and status register whose offset is equal to the idx parameter. The value written in the register is the bitwise OR between the result of the read cycle and the content of the data_p parameter.
This is equivalent to perform the following operation:
  tsc_csr_rd( idx, &tmp);
  tmp |= *data_p;
  tsc_csr_wr( idx, &tmp);
That function is useful to reset status bit in registers where they have to be overwritten to be cleared.

Parameters
idx	register index (address offset in PCI IO window)
data	bit field (32 bit) holding the bit to be set in the register

Return
0 if OK
< 0 in case of error

A set of registers in the PON are also available:
### TSC PON Access
#### PON Read
Prototype

#include <tsculib.h>

int
tsc_pon_read( int idx,
      int *data_p)

Description
Perform a 32 bit read cycle in order to return the current value of the PON register whose offset is equal to bit 0:12 of the idx parameter.

Parameters
idx	register index (address offset)
data_p pointer to a 32 bit integer to hold register content

Return
status of the read operation
< 0 if error

#### PON Write
Prototype

#include <tsculib.h>

int
tsc_pon_write( int idx,
        int *data_p);

Description
Perform a 32 bit write cycle in order to set the current value of the PON register whose offset is equal to the idx parameter.

Parameters
idx	register index
data_p	pointer to a 32 bit integer holding the value to be written

Return
Status of the write operation
< 0 if error

## Resources Access
A set of functions allows applications to perform read and write access both shared memory (SHM1, SHM2) and in the FPGA's user space (USR1, USR2).
### Shared memory access
#### Shared memory (SHM) Read
Prototype

#include <tsculib.h>

int
tsc_shm_read(uint shm_addr, char *buf, int len, int ds, int swap, int mem)

Description
Perform a read operation from the Shared memory. Parameters allow to select the SHM address (offset), the buffer to realize the operation, the size of the transfer, the type of data size, the swapping method and finally to choose the memory 1 or 2.

Parameters
shm_addr	address offset
buf	container for data
len	size of the transfer
ds	data size
swap	swap process
mem	space selection (1 or 2)

Return
status of the read operation
< 0 if error

#### Shared memory (SHM) Write
Prototype

#include <tsculib.h>

int
tsc_shm_write(uint shm_addr, char *buf, int len, int ds, int swap, int mem)

Description
Perform a write operation to the Shared memory. Parameters allow to select the SHM address (offset), the buffer to realize the operation, the size of the transfer, the type of data size, the swapping method and finally to choose the memory 1 or 2.

Parameters
shm_addr	address offset
buf	container for data
len	size of the transfer
ds	data size
swap	swap process
mem	space selection (1 or 2)

Return
Status of the write operation
< 0 if error

### FPGA user Access
#### FPGA user Read
Prototype

#include <tsculib.h>

int
tsc_usr_read(uint usr_addr, char *buf, int len, int ds, int swap, int mem)

Description
Perform a read operation from the FPGA's user space. Parameters allow to select the USR address (offset), the buffer to realize the operation, the size of the transfer, the type of data size, the swapping method and finally to choose the FPGA's user space 1 or 2.

Parameters
usr_addr	address offset
buf	container for data
len	size of the transfer
ds	data size
swap	swap process
mem	space selection (1 or 2)

Return
status of the read operation
< 0 if error

#### FPGA user Write
Prototype

#include <tsculib.h>

int
tsc_usr_write(uint usr_addr, char *buf, int len, int ds, int swap, int mem)

Description
Perform a write operation to the FPGA's user space. Parameters allow to select the USR address (offset), the buffer to realize the operation, the size of the transfer, the type of data size, the swapping method and finally to choose the FPGA's user space 1 or 2.

Parameters
usr_addr	address offset
buf	container for data
len	size of the transfer
ds	data size
swap	swap process
mem	space selection (1 or 2)

Return
Status of the write operation
< 0 if error

A global timer is available in the FPGA user space to sync and measure the time.

### FPGA user Timer
#### Timer start
Prototype

#include <tsculib.h>

int
tsc_timer_start(int mode, int msec)

Description
Perform a timer start (time is reset to 0).

Parameters
mode	mode for the timer
msec	timer value

Return
status of the operation
< 0 if error

#### Timer stop
Prototype

#include <tsculib.h>

int
tsc_timer_stop(void)

Description
Perform a timer stop after a timer start.

Parameters
none

Return
Status of the operation
< 0 if error

#### Timer read
Prototype

#include <tsculib.h>

int
tsc_timer_read(struct tsc_time *tm)

Description
Perform a timer read to acquire time.

Parameters
tm	timer structure

Return
Status of the operation
< 0 if error

#### Timer restart
Prototype

#include <tsculib.h>

int
tsc_timer_restart(void)

Description
Perform a timer restart after a stop operation (timer restart from stop value and continue to count).

Parameters
none

Return
Status of the operation
< 0 if error

A set of functions allow to use FIFOs/Mailbox and Semaphores to interface with another processes.

### FIFOs
#### FIFO initialization
Prototype

#include <tsculib.h>

int
tsc_fifo_init(int idx, int mode)

Description
Perform the initialization of the FIFO either in FIFO mode (0) either in MAILBOX mode (1).

Parameters
idx	FIFO identifier (0 to 7)
mode	FIFO mode (0) or MAILBOX mode (1)

Return
status of the operation
< 0 if error

#### FIFO status
Prototype

#include <tsculib.h>

int
tsc_fifo_status(uint idx, uint *sts)

Description
This function allows to get the status of the FIFO.

Parameters
idx	FIFO identifier (0 to 7)
sts	Status of the FIFO

Return
Status of the operation
< 0 if error

#### FIFO clear
Prototype

#include <tsculib.h>

int
tsc_fifo_clear(uint idx, uint *sts)

Description
This function allows to clear a selected FIFO.

Parameters
idx	FIFO identifier
sts	Status of the FIFO

Return
Status of the operation
< 0 if error

#### FIFO read
Prototype

#include <tsculib.h>

int
tsc_fifo_read(uint idx, uint *data, uint wcnt, uint *sts)

Description
Perform a read operation on a FIFO.

Parameters
idx	FIFO identifier
data	Data read
wcnt	Number of words to read
sts	Status of the FIFO

Return
Status of the operation
< 0 if error

#### FIFO write
Prototype

#include <tsculib.h>

int
tsc_fifo_write(uint idx, uint *data, uint wcnt, uint *sts)

Description
Perform a write operation on a selected FIFO.

Parameters
idx	FIFO identifier
data	Data to write
wcnt	Number of words to write
sts	FIFO status

Return
Status of the operation
< 0 if error

### SEMAPHOREs
#### SEMAPHORE status
Prototype

#include <tsculib.h>

int
semaphore_status(uint *sts)

Description
Acquire the status of the semaphore.

Parameters
sts	Status of the semaphore

Return
status of the operation
< 0 if error

#### SEMAPHORE release
Prototype

#include <tsculib.h>

int
semaphore_release(uint idx)

Description
Release a specific semaphore.

Parameters
idx	Semaphore identifier (0 to 15)

Return
Status of the operation
< 0 if error

#### SEMAPHORE get
Prototype

#include <tsculib.h>

int
semaphore_get(uint idx, uint *tag)

Description
Get a semaphore and set the semaphore with a specific tag.

Parameters
idx	Semaphore identifier (0 to 15)
tag	Specific tag for the semaphore (7 bits)

Return
Status of the operation
< 0 if error

### System Monitoring
Xilinx Artix-7 FPGA implements a set of register to perform system monitoring of parameters such as temperature and external power supplies.
Please refer to Xilinx documentation for register description.
#### SMON Read
Prototype

#include <tsculib.h>

int
tsc_smon_rd( int idx,
        int *data_p)

Description
Read from the Xilinx SMON register at offset idx and store the result in location pointed by data_p

Parameters
idx	register index
data_p data pointer to hold result of SMON read

Return
0 if OK
< 0 in case of error

#### SMON Write
Prototype

#include <tsculib.h>

int
tsc_smon_write( int idx,
   int *data_p);

Description
Write in Xilinx ARTIX7 SMON register space at offset idx.

Parameters
idx	register index
data_p pointer to 32 bit integer holding the data to be written

Return
0 if OK
< 0 in case of error

### PCIe End Point Control
Xilinx Artix-7 FPGA implements a set of registers to configure the PCIe End Point. The tsc_pciep_xxx() functions allow to read/write these registers.
#### PCIep Read
Prototype

#include <tsculib.h>

int
tsc_pciep_read( int idx,
        int *data_p)

Description
Read from the Xilinx PCIep register space at offset idx and store the result in location pointed by data_p

Parameters
idx	register index
data_p data pointer to hold result of PCIep read

Return
0 if OK
< 0 in case of error

#### PCIep Write
Prototype

#include <tsculib.h>

int
tsc_pciep_write( int idx,
    int *data_p);

Description
Write in Xilinx ARTIX7 PCIep register space at offset idx the content of data_p.

Parameters
idx	register index
data_p pointer to 32 bit integer holding the data to be written

Return
0 if OK
< 0 in case of error

## TSC Resource Mapping
The TSC acts as a bridge between the following address spaces:
- PCI tree
- Shared Memory
- USER memory
Going from one space to another implies the initialization of address translation tables in order to map source addresses to destination addresses. A set of functions allows application to dynamically create, modify, and destroy these address translation windows.
### Allocating a New Address Translation Window
Prototype

#include <tsculib.h>
#include <tscioctl.h>

void
tsc_map_alloc( struct tsc_ioctl_map_win *map_p)

Description
That function allows to create an address window in a local space pointing to a remote area in a destination space specified in the mode field of the mapping data structure given as parameter.

Parameters

map_p	pointer to a tsc_ioctl_map_win data structure initialized with the mapping parameters (see §Managing Remote Resources).
	map_p->req.rem_addr	base address of remote area to be mapped
	map_p->req.size	Size (in bytes) of remote area to be mapped
	map_p->req.loc_addr	If MAP_FLAG_FORCE is set, ask mapper to use loc_addr as local address for base offset of translation window.
	map_p->req.mode.sg_id	Identifier of mapping table to be used
	MAP_ID_MAS_PCIE_MEM → PCIe master mapper (MEM space) / MAP_ID_MAS_PCIE_PMEM → PCIe master mapper (PMEM space)
	map_p->req.mode.space	Remote space
	MAP_SPACE_PCIE1 → PCI Express tree 1 is the destination space / MAP_SPACE_PCIE2 → PCI Express tree 2 is the destination space / MAP_SPACE_SHM1 → Shared Memory 1 is the destination space / MAP_SPACE_SHM2 → Shared Memory 2 is the destination space / MAP_SPACE_USR1 → FPGA user 1 is the destination space / MAP_SPACE_USR2 → FPGA user 2 is the destination space
	map_p->req.mode.am	Address Modifier
	map_p->req.mode.swap	Data swapping mode
	MAP_SWAP_NO → No hardware data swapping / MAP_SWAP_AUTO → Hardware auto swapping
	map_p->req.mode.flags	Mapping flags
	MAP_FLAG_FORCE → Force translation window base offset

Return
0	Mapping successful / tsc_ioctl_map_win data structure has been updated with the mapping parameters.
	map_p->pg_idx	Page index in translation table used to create the address mapping
	map_p->req.loc_addr	Address in local space pointing to requested remote address
-1	Mapping not successful

### Getting Mapping Parameters of an Address Translation Window

Prototype

#include <tsculib.h>
#include <tscioctl.h>

int
tsc_map_get( struct tsc_ioctl_map_win *map_p)

Description
That function allows to get the mapping parameter of an existing translation window identified by pg_idx and created in the mapper identified by sg_id.

Parameters

map_p	pointer to a tsc_ioctl_map_win data structure initialized with the mapping parameters.
	map_p->pg_idx	base address of remote area to be mapped
	map_p->req.mode.sg_id	Identifier of mapping table to be used

Return
0	Mapping successful / tsc_ioctl_map_sts data structure has been updated with the mapping parameters.
	map_p->sts.loc_base	Base address on the local bus of the translation window
	map_p->sts.rem_base	Address in remote space pointed by loc_base
	map_p->sts.size	Actual window size (in bytes) of the translation window
	map_p->sts.mode.hw	Hardware mapping mode
< 0	pg_idx or sg_id does not refer to a valid translation window

### Freeing an Address Translation Window
Prototype

#include <tsculib.h>
or
#include <tscioctl.h>

void
tsc_map_free( struct tsc_ioctl_map_win *map_p)

Description
That function frees a mapping window previously allocated by a call to tsc_map_alloc(). The field pg_idx and sg_id of the tsc_ioctl_map_win data structure are used by the tsc driver to identify the window to be freed.

Parameters

map_p	pointer to a tsc_ioctl_map_win data structure initialized with the mapping parameters.
	map_p->pg_idx	Offset (as returned by tsc_map_alloc()) of mapping window to be freed
	map_p->req.mode.sg_id	Identifier of mapping table to be used

Return
0	Mapping window successfully freed
< 0	Invalid mapping window

### Modifying an Address Translation Window
Prototype

#include <tsculib.h>
#include <tscioctl.h>

void
tsc_map_modify( struct tsc_ioctl_map_win *map_p)

Description
That function modifies a mapping window previously allocated by a call to tsc_map_alloc(). The field sg_id and pg_idx of the tsc_ioctl_map_pg data structure are used by the tsc driver to identify the window to be modified.

Parameters
map_p	pointer to a tsc_ioctl_map_pg data structure initialized with the mapping parameters.
	map_p->pg_idx	Page index (as returned by tsc_map_alloc()) of mapping window to be modified
	map_p->req.mode.sg_id	Identifier of mapping table to be modified
	map_p->req.rem_addr / map_p->req.size / map_p->req.mode	Parameters to be modified (see tsc_map_alloc()). Beware that the rem_addr and size must be compatible with the window size previously allocated.

Return
0	Mapping window successfully freed
< 0	Invalid mapping window parameters

### Getting a List of all Allocated Address Translation Windows

Prototype

#include <tsculib.h>
#include <tscioctl.h>

int
tsc_map_read( struct tsc_ioctl_map_ctl *ctl_p)

Description
That function updates the tsc_ioctl_map_ctl data structure with the control parameters of the translation table identified by the sg_id field.

Parameters
ctl_p	pointer to a tsc_ioctl_map_ctl data structure.
	ctl_p->sg_id	Identifier of mapping table
	ctl_p->map_p	Pointer to a tsc_map_blk[] data structure big enough to hold a full image of the address translation table. The size of that table shall be equal to / ctl_p->pg_num * sizeof( stuct tsc_map_blk) / If that pointer is set to NULL, only control fields in the tsc_ioctl_map_ctl data structure are updated.

Return

0	tsc_ioctl_map_pg data structure pointed by ctl_p parameter has been updated with the table control parameters.
	ctl_p->pg_num	Number of pages in the address translation table
	ctl_p->pg_size	Page size
	ctl_p->win_base	Local address of the first page of the translation window in the table.
	ctl_p->win_size	Total size occupied by the mapper on the local bus
< 0	If table identifier or data pointer invalid

### Clearing all Allocated Address Translation Windows

Prototype

#include <tsculib.h>
#include <tscioctl.h>

int
tsc_map_clear( struct tsc_ioctl_map_ctl *ctl_p);

Description
That function clears all mapping window previously allocated by a call to tsc_map_alloc(). The field sg_id is used by the tsc driver to identify the table to be cleared.

Parameters
ctl_p	pointer to a tsc_ioctl_map_ctl.
	ctl_p->sg_id	Identifier of mapping table

Return

0	If successful
-1	If table identifier invalid

## Kernel Buffers
Buffer suitable for DMA access shall be allocated using special kernel function to make sure they are locked in memory and visible from the PCI Express. This operation is done by the device driver using the tsc_IOCTL_BUF_ALLOC ioctl() command.
Once a buffer has been allocated, its kernel address can be used to map it in user's space using the /dev/kmem device. That operation can only be done in superuser mode.
### Allocating a Buffer in System Memory Suitable for DMA
Prototype

#include <tsculib.h>
#include <tscioctl.h>

void *
tsc_kbuf_alloc( struct tsc_ioctl_kbuf_req *buf_p)

Description
That function updates the tsc_ioctl_kbuf_req data structure with the parameters of the buffer allocated by the kernel in system memory. This call is operating system dependent.

Parameters
buf_p	pointer to a tsc_ioctl_kbuf_req data structure.
	buf_p->size	Size of the buffer to be allocated

Return

0	tsc_ioctl_kbuf_req data structure updated with the parameters of the buffer allocated
	buf_p->k_base	Buffer kernel base address (suitable for subsequent call to mmap() function using /dev/kmem device)
	buf_p->b_base	Buffer bus base address (suitable for DMA parameters)
NULL	Buffer was not allocated

### Freeing an Allocated Buffer

Prototype

#include <tsculib.h>
#include <tscioctl.h>

int
tsc_kbuf_free( struct tsc_ioctl_kbuf_req *buf_p)

Description
That function free a buffer previously allocated by a call to tsc_kbuf_alloc(). This call is operation system dependent.

Parameters

buf_p	pointer to a tsc_ioctl_buf data structure initialized with the buffer parameters.
	buf_p->k_base	Kernel base address (as returned by tsc_buf_alloc()) of the buffer to be freed
	buf_p->b_base	Bus base address (as returned by tsc_buf_alloc()) of the buffer to be freed
	buf_p->size	Size (as returned by tsc_buf_alloc()) of the buffer to be freed

Return
0	Buffer successfully freed
< 0	Invalid buffer parameters

### Reading from a Kernel Buffer
Prototype

#include <tsculib.h>
#include <tscioctl.h>

int
tsc_kbuf_read( void_*k_addr,
        char *buf,
        uint size)

Description
That function allows to move data from a kernel buffer suitable for DMA access to a buffer allocated in the application space.

Parameters

k_addr	Kernel buffer address
buf	Pointer to the user buffer
size	Number of bytes to read

Return
0	Data transfer successful
< 0	See ioctl() error codes

### Writing to a Kernel Buffer
Prototype

#include <tsculib.h>
#include <tscioctl.h>

int
tsc_kbuf_write( void_*k_addr,
        char *buf,
        uint size)

Description
That function allows to move data from a buffer allocated in the application space to a kernel buffer suitable for DMA access.

Parameters

k_addr	Kernel buffer address
buf	Pointer to the user buffer
size	Number of bytes to be written

Return
0	Data transfer successful
< 0	See ioctl() error codes

## DMA Transfer
### Performing a DMA Transfer
Prototype

#include <tsculib.h>
#include <tscioctl.h>

int
tsc_dma_move( struct tsc_ioctl_dma_req *req_p)

Description
This is the generic function to perform DMA transfers. Transfer parameters shall be loaded in the tsc_ioctl_dma_req data structure.
Data transfer is performed between two different spaces. The address parameters are address offset within the specified space.
When performing data transfer on buses such PCIe, blocks are divided in packets whose size depend on the characteristics of the bus or the target device. The maximum packet size to be used by the DMA engine shall be defined in the size parameters. By default it is 128 bytes

Parameters

req_p	pointer to a tsc_ioctl_dma_req data structure initialized with the transfer parameters.
	req_p->des_addr	DMA transfer destination address
	req_p->des_space	DMA transfer destination space
	DMA_SPACE_PCIE → PCI Express (1, 2) / DMA_SPACE_SHM → shared memory (1, 2) / DMA_SPACE_USR → USR space (1, 2) / DMA_SPACE_WS → 16 bit byte swapping (OR with DMA_SPACE_XXX) / DMA_SPACE_DS → 32 bit byte swapping (OR with DMA_SPACE_XXX) / DMA_SPACE_QS → 64 bit byte swapping (OR with DMA_SPACE_XXX)
	req_p->des_mode	DMA transfer destination mode
	DMA_PCIE_TC0 → PCI Express Traffic Class 0 / DMA_PCIE_TC1 → PCI Express Traffic Class 1 / DMA_PCIE_TC2 → PCI Express Traffic Class 2 / DMA_PCIE_TC3 → PCI Express Traffic Class 3 / DMA_PCIE_TC4 → PCI Express Traffic Class 4 / DMA_PCIE_TC5 → PCI Express Traffic Class 5 / DMA_PCIE_TC6 → PCI Express Traffic Class 6 / DMA_PCIE_TC7 → PCI Express Traffic Class 7 / DMA_PCIE_RR1 → PCI Express 1 outstanding request / DMA_PCIE_RR2 → PCI Express 2 outstanding request / DMA_PCIE_RR3 → PCI Express 3 outstanding request
	req_p->src_addr	DMA transfer source address
	req_p->src_space	DMA transfer source space
	req_p->src_mode	DMA transfer source mode
	req_p->size	Bits 23:0 encode the DMA transfer size (in bytes). Bits 31:30 encode the max packet size used by the DMA engine.
	DMA_SIZE_PKT_128 → maximum DMA packet size 128 Bytes / DMA_SIZE_PKT_256 → maximum DMA packet size 256 Bytes / DMA_SIZE_PKT_512 → maximum DMA packet size 512 Bytes / DMA_SIZE_PKT_1k → maximum DMA packet size 1 KBytes
	req_p->start_mode	DMA starting mode
	DMA_START_CHAN(chan) → use DMA channel chan (0 or 1)
	req_p->intr_mode	Interrupt mode
	DMA_INTR_ENA → enable interrupt
	req_p->wait_mode	Wait mode
	DMA_WAIT_INTR → wait for interrupt / DMA_WAIT_1MS → set 1 msec scale / DMA_WAIT_10MS → set 10 msec scale / DMA_WAIT_100MS → set 100 msec scale / DMA_WAIT_1S → set 1 sec scale / DMA_WAIT_10S → set 10 sec scale / DMA_WAIT_100S → set 100 sec scale
	req_p->dma_status	DMA current status updated by the driver. If a DMA interrupt has been detected, bit 31:16 hods the interrupt source identifier
	DMA_STATUS_RUN_RD0 → set when DMA read engine #0 is started / DMA_STATUS_RUN_RD1 → set when DMA read engine #1 is started / DMA_STATUS_RUN_WR0 → set when DMA write engine #0 is started / DMA_STATUS_RUN_WR1 → set when DMA write engine #1 is started / DMA_STATUS_DONE → set when the DMA interrupt is detected / DMA_STATUS_WAITING → set when the driver start waiting / DMA_STATUS_ENDED → set when the driver finish waiting / DMA_STATUS_ERR → set if an error has been detected / DMA_STATUS_TMO → set if a timeout has been detected

Return
0	DMA transfer ended
< 0	Invalid transfer parameters

### Getting the Status of a DMA Transfer
Prototype

#include <tsculib.h>

int
tsc_dma_status( struct tsc_ioctl_dma_sts *sts)

Description
That function fills tsc_ioctl_dma_sts data structure with the current status of a DMA controller. Basically that data structure contains the current value of the 2*4 hardware registers controlling the DMA engine (refer to hardware description of the DMA controller).

Parameters
sts	Pointer to a tsc_ioctl_dma_sts data structure
	sts->dma.chan → DMA channel index (0, 1, 2, 3)

Return
0	sts data structure filled with current value of DMA HW registers
	sts->dma.status	Current status of DMA transfer
	sts->dma.state	DMA channel current state / DMA_STATE_IDLE / DMA_STATE_ALLOCATED / DMA_STATE_STARTED / DMA_STATE_WAITING / DMA_STATE_DONE
	sts->rd_csr	Read engine CSR
	sts->rd_ndes	Read engine next descriptor address
	sts->rd_cdes	Read engine current descriptor address
	sts->rd_cnt	Read engine word counter & HW status
	sts->wr_csr	Write engine CSR
	sts->wr_ndes	Write engine next descriptor address
	sts->wr_cdes	Write engine current descriptor address
	sts->wr_cnt	Write engine word counter & HW status
< 0	If error

### Wait for a DMA Transfer to Complete
Prototype

#include <tsculib.h>

int
tsc_dma_wait( struct tsc_ioctl_dma_req *req_p)

Description
That function can be called after a tsc_dma_move() has been issued. It takes as parameters a pointer to the request structure used for that call..

Parameters
req_p	Pointer to the tsc_ioctl_dma_req data structure used for the tsc_dma_move(). / The req_p->wait_mode shall be set with the wait parameters:
	DMA_WAIT_INTR → wait for interrupt / DMA_WAIT_1MS → set 1 msec scale / DMA_WAIT_10MS → set 10 msec scale / DMA_WAIT_100MS → set 100 msec scale / DMA_WAIT_1S → set 1 sec scale / DMA_WAIT_10S → set 10 sec scale / DMA_WAIT_100S → set 100 sec scale

Return
0	If OK
< 0	If error

### Allocate/Free DMA Channel
Prototype

#include <tsculib.h>

int
tsc_dma_alloc( int chan)
tsc_dma_free( int chan)

Description
That function allocates/free a DMA channel to/from the current task. In order for a task to use a DMA channel, the channel shall be free or already allocated to that task.
When a task owns a channel it shall explicitly fee it. When a task exits, all channels allocated to that task are freed.

Parameters
chan	DMA channel index (0, 1, 2, 3)

Return
0	If OK
< 0	If error

### Resetting a DMA channel
Prototype

#include <tsculib.h>

int
tsc_dma_clear( int chan)

Description
That function resets a DMA channel back in the idle state

Parameters
chan	DMA channel index (0 or 1)

Return
0	If OK
< 0	If error