TscMon / User's Manual

Command Interpreter for TSC

IOxOS Technologies SA / 4, Chemin des Fontenailles / CH-1196 Gland / SWITZERLAND

IOxOS Technologies SA universal property / The content of this document is the property of IOxOS Technologies SA. It is supplied in confidence and commercial security on its contents must be maintained. It must not be used for any purpose other than that for which it is supplied nor may information contained in it be disclosed to un-authorized persons. It must not be reproduced in whole or part without permission in writing from IOxOS Technologies SA.

Version Control
Version	Date	Chapter and section modifications	Author	Checked	Approved
1.0.0	20 Nov 2017	Initial version	JFG / XP	IGA	JBO

Author references
Initial	Name	Company	Comments
[JBO]	Joel BOVIER	IOxOS Technologies SA
[JFG]	Jean-Francois GILOT	IOxOS Technologies SA
[IGA]	Iván GARCÍA-ALFONSO	IOxOS Technologies SA
[XP]	Xavier PAILLARD	IOxOS Technologies SA

# Introduction
## Purpose
This manual is intended for use by system designers, software developers and support personnel.
It is recommended that the reader has a reasonable background in PCI architecture, including experience or knowledge of I/O buses and related protocols.

## Acronyms and Abbreviations
Acronym	Definition
DMA	Direct Memory Access
IO	Input/Output
PC	Personal Computer
PCI	Peripheral Component Interconnect
PCIe	PCI Express

Table 1.1: Acronyms

## References

Reference	Title	Version	Date	Owner
	PCI Local Bus Specification	3.0	Aug 12,2002	PCI-SIG
	PCIe Base Specification	2.0	Jan 4, 2007	PCI-SIG

Table 1.2: References

# TSC Command Interpreter
## Introduction
TscMon is an application linked with the TSC user's library. It allows the user to perform interactively a set of command to operate the TSC interface. Once the tsc driver has been inserted in the kernel, TscMon is very useful to set-up and debug various configurations.
### Command Syntax
TscMon command syntax is as follow:
cmd.ext para#1:m#1 para#2:m#2 …
where
cmd is the command name
ext is a command extension (optional)
para#i are the command parameters
m#i are the parameter modifiers (optional)
The help command displays a list of all allowed command names.
### Command Parameters
TscMon parameters can be strings, integers, ranges or data set. By default integers are interpreted and displayed as hexadecimal numbers.
Some commands takes address range and data set parameters.
#### Address and Address Range
Ranges shall be in the form of
start..end
or
start..end:space
where
start and end are integers
space is an address space identifier
#### Data and Data Set
data set parameter shall be in the form of
c:data..para
where c is a ascii character identifying the set:
  r:<seed> → fill range with pseudo random data
  s:<start>..<inc> → fill range with a ramp
  w:<data>..<mask> → fill range with a walking pattern
For random data set, the rand() function is used with <seed> parameter as seed for the random generator. The first data of the set is the <seed> parameter
The ramp data set starts with the <start> parameter and <inc> parameter is used as increment to generate the next data in the set.
The walking pattern data set is calculated according to the following formula:
    <data> XOR <mask>
To calculate the next data in the set, the mask is left rotated by 1 over the data size. This allows to generate a 32 bit walking 1 with
  w:ffffffff..fffffffe
and a walking 0 with
  w:ffffffff..1
### Starting TscMon
TscMon is started by invoking the TscMon binary file from a shell

root@IFC1410: ./TscMon

        _______ __ __
        |__ __| | \/ |
        | |___ ___| \ / | ___ _ __
        | / __|/ __| |\/| |/ _ \| '_ \
        | \__ \ (__| | | | (_) | | | |
        |_|___/\___|_| |_|\___/|_| |_|

     +------------------------------------------+
     | IOxOS Technologies Copyright 2015-2017 |
     | TscMon - CENTRAL 1001 diagnostic tool |
     | Version 1.40 - Dec 1 2017 11:11:30 |
     | FPGA Built Nov 28 2017 13:32:35 |
     | FPGA Sign 08111701 |
     | Driver IFC1410 Version 1.40 |
     | ******* Official release 1.4.3 ******* |
     +------------------------------------------+

1:TscMon>

TscMon supports online help. The help or ? command displays the list of available commands. It can take any command name as parameter.
1:TscMon>help
 acq1430 adc3110 adc3117 alias
 ci cmp conf cp1
 cp2 cr cs1 cs2
 cs cu1 cu2 cu
 dc di dk dma
 dm dp1 dp2 dr
 ds1 ds2 ds du1
 du2 du fifo fk
 fp1 fp2 fm fs1
 fs2 fs fu fu1
 fu2 help his i2c
 kbuf lmk lp1 lp2
 ls1 ls2 ls lu2
 lu1 lu map mbox
 pc pi pk pm
 pp1 pp2 pr ps1
 ps2 ps pu1 pu2
 pu rtm semaphore set
 smem tdma timer tinit
 tkill tlist tstatus tstart
 tstop tset tp1 tp2
 ts1 ts2 ts tu1
 tu2 tu twait
2:TscMon>? help
  Display list of commands or syntax of command <cmd>
  help
  help <cmd>

During its initialization phase, TscMon allocates a 1 Mbyte data buffer in kernel space.

TscMon provides a set of commands to perform CPU read/write accesses from/to:
- the TSC shared memory (embedded FPGA memory and DDR3 memory)
- the kernel buffer allocated in local host system memory

#### Specifics TscMon commands
Several commands exist to execute specifics actions in TscMon application:

– “@” This command allows to load and execute a TscMon script :
Example
24:TscMon>@myscript.xpm
Start execution of script file myscript
24:TscMon>ds.w 100000
device: 0
0x00100000 : 00000000 00000000 00000000 00000000 ................
0x00100010 : 00000000 00000000 00000000 00000000 ................
0x00100020 : 00000000 00000000 00000000 00000000 ................
0x00100030 : 00000000 00000000 00000000 00000000 ................

The content of the script is:
ds.w 100000

– “$” This command allows to execute a Linux shell command :
Example
17:TscMon>$uname -a
OS command: <uname -a>
Linux IFC1410 4.1.8-rt8+gbd51baf #39 SMP Fri Jan 13 17:02:41 CET 2017 ppc64 GNU/Linux
return code: 0

– “&” This command allows to repeat the command (type a key to stop the repeat) :
Example
5:TscMon>&dma.0 start 100000:2 0:8 1000
Entering loop mode [enter any character to stop loop]...
OK -> status = 24000114
OK -> status = 24000114
OK -> status = 24000114
OK -> status = 24000114
…

– “+” This command allows to call a specific alias :
Example
2:TscMon>alias set myalias "ds.w 100000"
3:TscMon>alias show
alias list:
myalias "ds.w 100000"
4:TscMon>+myalias
ds.w 100000
device: 0
0x00100000 : ffff0000 ffff0000 0000ffff ffff0000 ................
0x00100010 : 00000000 ffffffff ffff0000 00000000 ................
0x00100020 : 0000ffff ffffffff ffff0000 ffff0000 ................
0x00100030 : 0000ffff ffff0000 00000000 ffffffff ................

– “!” This command allows to call a specific command according to the command history :
Example
1:TscMon>ds.w 100000
device: 0
0x00100000 : ffff0000 ffff0000 0000ffff ffff0000 ................
0x00100010 : 00000000 ffffffff ffff0000 00000000 ................
0x00100020 : 0000ffff ffffffff ffff0000 ffff0000 ................
0x00100030 : 0000ffff ffff0000 00000000 ffffffff ................
2:TscMon>dm.w 100
device: 0
0x00000100 : 00000000 00000000 00000000 00000000 ................
0x00000110 : 00000000 00000000 00000000 00000000 ................
0x00000120 : 00000000 00000000 00000000 00000000 ................
0x00000130 : 00000000 00000000 00000000 00000000 ................
3:TscMon>history
   0 ds.w 100000
   1 dm.w 100
4:TscMon>!1
dm.w 100
device: 0
0x00000100 : 00000000 00000000 00000000 00000000 ................
0x00000110 : 00000000 00000000 00000000 00000000 ................
0x00000120 : 00000000 00000000 00000000 00000000 ................
0x00000130 : 00000000 00000000 00000000 00000000 ................

## Command List
Command	Description	Reference
acq1430	ACQ1430 operations	$2.2.1
adc3110	ADC3110 operations	$2.2.2
adc3117	ADC3117 operations	$2.2.3
alias	Create command aliases	$2.2.4
ci	Compare with mask the content of IFC PON register with data	$2.2.5
cmp	Compare content of two data buffer	$2.2.6
conf	Show TSC current configuration	$2.2.7
cp1, cp2	Compare with mask the content of a location in PCI tree	$2.2.8
cr	Compare with mask the content of CSR register with data	$2.2.9
cs, cs1, cs2	Compare with mask the content of a location in SHM with data	$2.2.10
cu, cu1, cu2	Compare with mask the content of a location in USR space with data	$2.2.11
dc	Display content of a set of TSC PCI CFG registers	$2.2.12
di	Display content of a set of IFC PON registers	$2.2.13
dm, dk	Display content of kernel buffer in System Memory	$2.2.14
dma	Perform DMA operation	$2.2.15
dp1, dp2	Display content in PCI tree	$2.2.16
dr	Display content of a set of TSC CSR registers	$2.2.17
ds, ds1, ds2	Display content of Shared Memory	$2.2.18
du, du1, du2	Display content of USR space	$2.2.19
fifo	FIFOs operations	$2.2.20
fm, fk	Fill kernel buffer in system memory	$2.2.21
fp1, fp2	Fill PCI tree addresses with data	$2.2.22
fs, fs1, fs2	Fill data buffer in TSC shared memory	$2.2.23
fu, fu1, fu2	Fill USR space with data	$2.2.24
help	Display list of commands or syntax of command <cmd>	$2.1
his	Display history of commands	$2.2.25
i2c	Perform i2c command	$2.2.26
kbuf	TSC kernel buffer operations	$2.2.27
lmk	Read/write LMK04803 registers	$2.2.28
lp1, lp2	Read/write loop from/to PCI addresses	$2.2.29
ls, ls1, ls2	Read/write loop from/to shared memory	$2.2.30
lu, lu1, lu2	Read/write loop from/to user area	$2.2.31
map	TSC address mapping operations	$2.2.32
mbox	MTCA.4 PON mailbox operations	$2.2.33
pc	Read/write data from/to TSC PCI configuration space	$2.2.34
pi	Read/write data from/to TSC IFC PON register	$2.2.35
pm, pk	Read/write data from/to TSC system memory	$2.2.36
pp1, pp2	Read/write data from/to PCI tree address	$2.2.37
pr	Read/write data from/to TSC register	$2.2.38
ps, ps1, ps2	Read/write data from/to TSC shared memory	$2.2.39
pu, pu1, pu2	Read/write data from/to FPGA USR space	$2.2.40
rtm	MTCA.4 RTM operations	$2.2.41
semaphore	Semaphores operations	$2.2.42
set	Select central or io device	$2.2.43
smem	Perform specific command on SMEM DDR memory	$2.2.44
!, @, $, &, +	Specific command	$2.1.3.1
tdma	Perform DMA operation using channel <x>	$2.2.45
tinit	Launch test suite	$2.2.46
tkill	Kill test suite	$2.2.47
tlist	Display a list of existing test	$2.2.48
tstatus	Show status of test suite	$2.2.49
tstart	Start execution of a test or a chain of tests	$2.2.50
tstop	Stop current test execution	$2.2.51
tset	Set test control parameter	$2.2.52
tp1, tp2	Perform read/write test in PCI tree address space	$2.2.53
ts, ts1, ts2	Perform read/write test on shared memory	$2.2.54
tu, tu1, tu2	Perform read/write test on FPGA USR memory	$2.2.55
twait	Wait for test to complete	$2.2.56

Table 2.1: TscMon Command List

### ACQ1430 operations
Command
ACQ1430 → ACQ1430 operations

Synopsis
acq1430.<x> <dev> read <reg>
acq1430.<x> <dev> write <reg> <data>
acq1430.<x> <dev> acqfif <offset> <size>
acq1430.<x> <dev> check <offset> <size>
acq1430.<x> <dev> acq<size> h:<file_his> d:<file_dat> t:<trig> s:<smem> c:<csr> a:<last_addr>
acq1430.<x> <dev> calib
acq1430.<x> <file> save <offset> <size>
acq1430.<x> tmp102 show
acq1430.<x> eeprom sign set
acq1430.<x> eeprom sign def b:<board> s:<serial> v:<ver> r:<rev>
acq1430.<x> eeprom dump
   where <x> = index
        <dev> = lmk, ads01, ads23, ads45, ads67, ads89
        <reg> = register
        <data> = data
        <offset> = offset of data buffer
        <size> = size of data buffer
        <file_his> = histogram filename
        <file_dat> = raw data filename

Description
This command allows to operate on the ACQ1430.

### ADC3110 operations
Command
ADC3110 → ADC3110 operations

Synopsis
adc3110.<x> <dev> read <reg>
adc3110.<x> <dev> write <reg> <data>
adc3110.<x> <dev> acqfif <offset> <size>
adc3110.<x> <dev> check <offset> <size>
adc3110.<x> <dev> acq<size> h:<file_his> d:<file_dat> t:<trig> s:<smem> c:<csr> a:<last_addr>
adc3110.<x> <file> save <offset> <size>
adc3110.<x> tmp102 show
adc3110.<x> eeprom sign set
adc3110.<x> eeprom sign def b:<board> s:<serial> v:<ver> r:<rev>
adc3110.<x> eeprom dump
   where <x> = index
        <dev> = lmk, ads01, ads23, ads45, ads67
        <reg> = register
        <data> = data
        <offset> = offset of data buffer
        <size> = size of data buffer
        <file_his> = histogram filename
        <file_dat> = raw data filename

Description
This command allows to operate on the ADC3110.

### ADC3117 operations
Command
ADC3117 → ADC3117 operations

Synopsis
adc3117.<x> <dev> read <reg>
adc3117.<x> <dev> write <reg> <data>
adc3117.<x> <dev> acq
adc3117.<x> <dev> save o:<offset> s:<size> h:<file_his> d:<file_dat>
adc3117.<x> <dev> temp
adc3117.<x> eeprom sign set
adc3117.<x> eeprom sign def b:<board> s:<serial> v:<ver> r:<rev>
adc3117.<x> eeprom dump
adc3117.<x> eeprom vref show
adc3117.<x> eeprom vref store
adc3117.<x> eeprom vref load
adc3117.<x> eeprom vref write <filename>
adc3117.<x> eeprom vref read <filename>
   where <x> = index
        <dev> = ads01, ads23, ads1, ads2, dac, xra01, xra23, xratrig, lmk, sy
        <reg> = register
        <data> = data

Description
This command allows to operate on the ADC3117.

### Command Aliases Management
Command
alias → create/destroy/display/save command aliases

Synopsis
  alias show
  alias clear
  alias set <alias> "<cmdline>"
  alias save <filename>
  alias load <filename>
     where <alias> = alias name to be created by the set operation
        <cmdline> = command line to be executed when $<alias> is entered
        <filename> = name of the file to be used by save and load

Description
The alias set operation allows to create an alias for a TscMon command. It takes two parameters

Examples
21:TscMon>alias set dma0_des "ds.ws 3000"
22:TscMon>alias set dma1_des "ds.ws 3800"
23:TscMon>alias show
alias list:
dma0_des "ds.ws 3000"
dma1_des "ds.ws 3800"
24:TscMon>$dma0_des
ds.ws 3000
0x00003000 : 0008a000 00010000 00001003 00000010 ................
0x00003010 : 77a00000 00000000 01010c6e 0049d47f ...w....n.....I.
0x00003020 : 0007e000 31010000 00001003 00000010 .......1........
0x00003030 : 20000000 00000000 01010c5d 0049d47f ... ....].....I.
25:TscMon>$dma1_des
ds.ws 3800
0x00003800 : 0008a000 00010000 00002003 00000010 ......... ......
0x00003810 : 77a00000 00000000 01000b16 004a2cf5 ...w.........,J.
0x00003820 : 0007e000 41010000 00002003 00000010 .......A. ......
0x00003830 : 20010000 00000000 01000b05 004a2cf5 ... .........,J.
26:TscMon>alias save myalias.ama
saving alias list in myalias.ama
27:TscMon>alias clear
28:TscMon>alias show
alias list:
29:TscMon>alias load myalias.ama
loading alias list from file "myalias.ama"
# TscMon alias list
dma0_des "ds.ws 3000"
dma1_des "ds.ws 3800"
#
30:TscMon>alias show
alias list:
dma0_des "ds.ws 3000"
dma1_des "ds.ws 3800"

### Compare with mask the content of IFC PON register with data
Command
ci → compare with mask the content of IFC pon register with data

Synopsis
ci <addr> <data> <mask>
   where <addr> = address offset in hexadecimal
        <data> = data in hexadecimal
        <mask> = mask in hexadecimal

Description
The ci command shall be used to perform cycles to compare the content of IFC PON register with a predefined data. It takes 3 parameters.
The first parameter shall be an address offset in PON.
The second parameter shall be the data to be used for the comparison.
The third parameter is the bit mask to be applied before comparing the address content with the data.

Examples
79:TscMon>di 0
00000000 : 73571410 02000000 00000000 00000000
81:TscMon>ci 0 73571410 ffffffff
0000 : 73571410 - 73571410 [ffffffff]
82:TscMon>ci 0 111 ffffffff
0000 : 00000111 - 73571410 [ffffffff] -> ERROR !!!

### Buffer Compare
Command
cmp → compare content of two data buffers

Synopsis
cmp <off1>:<sp1>[<idx1>] <off2>:<sp2>[<idx2>] <len>
   where <off> = address offset in hexadecimal
        <sp><idx> = buffer space [shm1, shm2, user1, user1, kbuf[0..7]]
        <len> = buffer size in bytes

Description
The cmp command shall be used to compare the content of two data buffers. These buffers can be located in the TSC shared memory [shm] or dynamically allocated in system memory [kbuf, k0->k7].
The cmp command takes three parameters, an address offset in the first buffer, an address offset in the second buffer and a length.
Address offset parameters are composed if three fields, an offset <off>, a space identifier <sp> an an optional index <id>.
Data in the two buffers are compared byte per byte starting at <off> up to <off> + <len>. If a mismatch is detected the error fag used script mode as exit condition is set.

Examples
9:TscMon>fs.w 10000..20000 s:12340000..4
10:TscMon>fm.w 0..10000 s:12340000..4
11:TscMon>cmp 10000:s 0:m 10000
Comparing data buffers.. -> OK
12:TscMon>ps.w 14004 deadface
13:TscMon>cmp 10000:s 0:m 10000
Comparing data buffers.. -> NOK
Error at offset 0x4000
buf#1 : 14000 : 12 34 40 00 de ad fa ce 12 34 40 08 12 34 40 0c
buf#2 : 4000 : 12 34 40 00 12 34 40 04 12 34 40 08 12 34 40 0c

### Show TSC Configuration
Command
conf → display TSC configuration

Synopsis
conf <operation> <resource>

   where <operation> operation to be perform
        show → display resource current configuration
        <resource> string identifying the TSC internal resource
        all → all available resources
        static → Static Options
device → Current device
        ddr → Show DDR3 information
identifiers → Front End PCIe switch (PEX8624)
        pcie → PCI Express End Point status
        msi → Interrupt counters
        smon → FPGA system monitoring

Description
The conf command allows to display the current configuration of the TSC interface.

Examples

5:TscMon>conf
   Static Options [0x0000e900]
      PCI IO size : 4 KBytes
      PCI MEM size : 128 MBytes
      PCI PMEM size : 512 MBytes
    PCIE identifier
      Board ID : Reserved
      Revision ID : 0
      PCIe EP : PCIe EP 1
   DDR3 configuration
      DDR3_SIZE : 4 Gbit [0x40000000]
   Identifiers
      FPGA eFUSE : 0x00000000
      FPGA Signature : 0x14111701
      FPGA Version : 0x00010101
      TOSCA Signature : 0x20160401
   PCIe MSI counters
      MSI Requests : 0x00002000
      MSI Armed : 0x00002000
      MSI Acknowledge : 0x00002000
      MSI Status : 0x00000020
   Artix7 System Monitoring
      Temperature : 50.69 [51.68 - 18.21]
      VCCint : 0.93 [0.93 - 0.93]
      VCCaux : 1.78 [1.78 - 1.78]
   Current device
      central

### Compare with mask the content of a location in PCI tree
Command
cp → compare with mask the content of a location in PCI tree with a data

Synopsis
cp.<ds> <addr> <data> <mask>
cp1.<ds> <addr> <data> <mask>
cp2.<ds> <addr> <data> <mask>

   where <ds> = b,s,w, (data size 1,2,4)
        <addr> = address offset in hexadecimal
        <data> = data in hexadecimal
        <mask> = mask in hexadecimal

Description
The cp command shall be used to perform cycles to compare the content of PCI tree with a predefined data. It takes 3 parameters.
The command extensions is made of 1 characters:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
The first parameter shall be an address offset in shared memory.
The second parameter shall be the data to be used for the comparison.
The third parameter is the bit mask to be applied before comparing the address content with the data.

### Compare with Mask the Content of an TSC CSR Register
Command
cr → compare data with content TSC CSR register

Synopsis
cr <reg> <data> <mask>

   where <reg> = register offset in hexadecimal
        <data> = data in hexadecimal
        <mask> = mask in hexadecimal

Description
The cr command shall be used to a read cycles targeted to an TSC CSR register and compare the result with a predefined data. Only bit set in the mask parameter are used for the comparison.
The command takes 3 parameters.
The first parameter shall be the address offset of the CSR register to be accessed.
The second parameter shall be the data to be used for the comparison.
The third parameter is the bit mask to be applied before comparing the address content with the data.

Examples
39:TscMon>cr.w 18 12011601 ffffffff
0018 : 12011601 - 12011601 [ffffffff]
40:TscMon>cr.w 18 12011602 ffffffff
0018 : 12011602 - 12011601 [ffffffff] -> ERROR !!!

### Compare with Mask the Content of a SHM Address
Command
cs → compare content of Shared Memory (1 or 2) with data

Synopsis
cs.<ds> <addr> <data> <mask>
cs1.<ds> <addr> <data> <mask>
cs2.<ds> <addr> <data> <mask>

   where <ds> = b,s,w, (data size 1,2,4)
        <addr> = SHM address offset in hexadecimal
        <data> = data in hexadecimal
        <mask> = mask in hexadecimal

Description
The cs command shall be used to perform cycles to compare the content of SHM address with a predefined data. It takes 3 parameters.
The command extensions is made of 1 characters:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
The first parameter shall be an address offset in shared memory.
The second parameter shall be the data to be used for the comparison.
The third parameter is the bit mask to be applied before comparing the address content with the data.

Examples
32:TscMon>ps.w 10000
0x00010000 : 00000000 -> 12345678
0x00010004 : 00000000 -> .
33:TscMon>cs.w 10000 12aa5678 ffffffff
00010000 : 12aa5678 - 12345678 [ffffffff] -> ERROR !!!
34:TscMon>cs.w 10000 12aa5678 ff0000ff
00010000 : 12aa5678 - 12345678 [ff0000ff]

### Compare with mask the content of a location in USR space with data
Command
cu → compare with mask the content of a location in USR space with data

Synopsis
cu.<ds> <addr> <data> <mask>
cu1.<ds> <addr> <data> <mask>
cu2.<ds> <addr> <data> <mask>

   where <ds> = b,s,w, (data size 1,2,4)
        <addr> = USR address offset in hexadecimal
        <data> = data in hexadecimal
        <mask> = mask in hexadecimal

Description
The cu command shall be used to perform cycles to compare the content of USR address with a predefined data. It takes 3 parameters.
The command extensions is made of 1 characters:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
The first parameter shall be an address offset in user space.
The second parameter shall be the data to be used for the comparison.
The third parameter is the bit mask to be applied before comparing the address content with the data.

Examples
50:TscMon>du1.w 0
device: 0
0x00000000 : 10000000 06111720 31434649 5f303134 ....... 1CFI_014
54:TscMon>cu1 0 10000000 ffffffff
device: 0
00000000 : 10000000 - 10000000 [ffffffff]
58:TscMon>cu1 0 1000ffff ffffffff
device: 0
00000000 : 1000ffff - 10000000 [ffffffff] -> ERROR !!!

### Display TSC PCI Configuration Registers
Command
dc → display content TSC PCI configuration registers

Synopsis
dc <start>[..<end>]

   where <start> = start offset in hexadecimal
        <end> = end offset in hexadecimal

Description
The dc command shall be used to display the content of TSC PCI Express End Point configuration registers.
The only parameter shall be a range of register address offsets whose content shall be displayed.

Examples
36:TscMon>dc.w 0

00000000 : 10017357 00100007 05800001 00000008
00000010 : e000000c 00000000 c0000000 c8000000
00000020 : 00002001 00000000 00000000 00025678
00000030 : 00000000 00000080 00000000 00000100

### Display content of a set of IFC PON registers
Command
di → display content of a set of IFC PON registers

Synopsis
di <start>[..<end>]
   where <start> = offset in hexadecimal of first register
        <end> = offset in hexadecimal of last register

Description
The di command shall be used to display the content of a set of IFC PON register.
The only parameter shall be a range of register address offsets whose content shall be displayed.

Examples
5:TscMon>di.w 0

00000000 : 73571410 02000000 00000000 00000000
00000010 : ffff0000 00000000 00000000 08111700
00000020 : 08000000 00000000 00000000 00000000
00000030 : 00000000 00000000 00000000 00000000

### Display Address Range from System Memory
Command
dm → display content of kernel buffer

Synopsis
dm.<ds>[<swap>] <start>[..<end>]

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start address in hexadecimal
        <end> = end address in hexadecimal

Description
The dm command shall be used to display the content of the kernel buffer allocated in system memory during the TscMon initialization phase.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character (optional) shall be s if the data are to be displayed byte swapped (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets whose content are to be displayed according to the data size chosen. Address offsets are offset related to the base address of the allocated buffer.

Examples
28:TscMon>dm.w 0
0x00000000 : 00010203 04050607 08090a0b 0c0d0e0f ................
0x00000010 : 10111213 14151617 18191a1b 1c1d1e1f ................
0x00000020 : 20212223 24252627 28292a2b 2c2d2e2f !"#$%&'()*+,-./
0x00000030 : 30313233 34353637 38393a3b 3c3d3e3f 0123456789:;<=>?

### DMA operations
Command
dma → perform a data transfer using DMA engines

Synopsis
dma.[<chan>] start <des_addr>:<des_space> <src_addr>:<src_space> <size>

   where <chan> = DMA channet (0 to 3)
        <des_addr> = address offset in the destination space
        <des_space> = destination space identifier
        <src_addr> = address offset in the source space
        <src_space> = source space identifier
        <size> = transfer size in byte

Description
The dma command allows to move data from a source address space identified by <src_space> to a destination address space identified by <des_space>. Allowed address space identifiers are:
   0 → PCI memory space
   2 → Shared Memory 1
   3 → Shared Memory 2
   4 → FPGA user's space 1
   5 → FPGA user's space 2
   8 → test buffer allocated in system memory
The <src_addr> and <des_addr> parameters are the address offsets in the source and destination spaces.
The <size> parameter is the transfer size in bytes.

Examples
Move 4 Kbytes from the embedded memory to the kernel buffer allocated by TscMon.

19:TscMon>dm.w 0
device: 0
0x00000000 : 00000000 00000000 00000000 00000000 ................
0x00000010 : 00000000 00000000 00000000 00000000 ................
0x00000020 : 00000000 00000000 00000000 00000000 ................
0x00000030 : 00000000 00000000 00000000 00000000 ................
20:TscMon>ds.w 10000
device: 0
0x00010000 : 00000000 00000004 00000008 0000000c ................
0x00010010 : 00000010 00000014 00000018 0000001c ................
0x00010020 : 00000020 00000024 00000028 0000002c ... ...$...(...,
0x00010030 : 00000030 00000034 00000038 0000003c ...0...4...8...<
21:TscMon>dma.0 start 0:8 10000:2 1000
OK -> status = 20000111
32:TscMon>dm.w 0
device: 0
0x00000000 : 00000000 00000004 00000008 0000000c ................
0x00000010 : 00000010 00000014 00000018 0000001c ................
0x00000020 : 00000020 00000024 00000028 0000002c ... ...$...(...,
0x00000030 : 00000030 00000034 00000038 0000003c ...0...4...8...<

Command
dma status → show the status of a DMA channel

Synopsis
dma[.<chan>] status

   where <start> = start offset in hexadecimal
        <end> = end offset in hexadecimal

Description
The dma status operation display the current state of the four hardware registers controlling the DMA channel

Examples
34:TscMon>dma.0 status
DMA#0 CSR registers
RD: 8048a000: 00000010 : 00003000: 80000000
WR: 8088e000: 00000010 : 00003020: 80000000

34:TscMon>dma.0 status
DMA#0 CSR registers
RD: 8048a000: 00000010 : 00003000: 80000000
WR: 8088e000: 00000010 : 00003020: 80000000

### Display content in PCI tree
Command
dp → display content in PCI tree

Synopsis
dp.<ds>[<swap>] <start>[..<end>]
dp1.<ds>[<swap>] <start>[..<end>]
dp2.<ds>[<swap>] <start>[..<end>]

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start address in hexadecimal
        <end> = end address in hexadecimal

Description
The dp command shall be used to display the content in PCI tree.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character (optional) shall be s if the data are to be displayed byte swapped (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets whose content are to be displayed according to the data size chosen. Address offsets are offset related to the base address in the PCI.

### Display TSC CSR Registers
Command
dr → display content TSC CSR registers

Synopsis
dr <start>[..<end>]

   where <start> = start offset in hexadecimal
        <end> = end offset in hexadecimal

Description
The dr command shall be used to display the content of TSC CSR registers.
The only parameter shall be a range of address offsets whose content shall be displayed.

Examples
32:TscMon>dr 0..20

00000000 : 0000e900 00000100 00000000 00000000
00000010 : 00000040 00000000 14111701 00010101

### Display Address Range from Shared Memory
Command
ds → display content of shared memory (1 or 2)

Synopsis
ds.<ds>[<swap>] <start>[..<end>]
ds1.<ds>[<swap>] <start>[..<end>]
ds2.<ds>[<swap>] <start>[..<end>]

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start address in hexadecimal
        <end> = end address in hexadecimal

Description
The ds command shall be used to display the content of the TSC Shared Memory.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character (optional) shall be s if the data are to be displayed byte swapped (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets whose content are to be displayed according to the data size chosen. Address offsets are offset related to the base address of the Shared Memory.

Examples
18:TscMon>ds.w 1000
0x00001000 : ff001000 ff001004 ff001008 ff00100c ................
0x00001010 : ff001010 ff001014 ff001018 ff00101c ................
0x00001020 : ff001020 ff001024 ff001028 ff00102c ... ...$...(...,
0x00001030 : ff001030 ff001034 ff001038 ff00103c ...0...4...8...<
19:TscMon>ds.ss 1000
0x00001000 : 00ff 0010 00ff 0410 00ff 0810 00ff 0c10 ................
0x00001010 : 00ff 1010 00ff 1410 00ff 1810 00ff 1c10 ................
0x00001020 : 00ff 2010 00ff 2410 00ff 2810 00ff 2c10 ... ...$...(...,
0x00001030 : 00ff 3010 00ff 3410 00ff 3810 00ff 3c10 ...0...4...8...<

### Display content of USR space
Command
du → display content of USR space

Synopsis
du.<ds>[<swap>] <start>[..<end>]
du1.<ds>[<swap>] <start>[..<end>]
du2.<ds>[<swap>] <start>[..<end>]

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start address in hexadecimal
        <end> = end address in hexadecimal

Description
The du command shall be used to display the content of the USR space.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character (optional) shall be s if the data are to be displayed byte swapped (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets whose content are to be displayed according to the data size chosen. Address offsets are offset related to the base address of the USR space.

Examples
18:TscMon>du.w 1000
0x00001000 : ff001000 ff001004 ff001008 ff00100c ................
0x00001010 : ff001010 ff001014 ff001018 ff00101c ................
0x00001020 : ff001020 ff001024 ff001028 ff00102c ... ...$...(...,
0x00001030 : ff001030 ff001034 ff001038 ff00103c ...0...4...8...<
19:TscMon>du.ws 1000
0x00001000 : 00ff 0010 00ff 0410 00ff 0810 00ff 0c10 ................
0x00001010 : 00ff 1010 00ff 1410 00ff 1810 00ff 1c10 ................
0x00001020 : 00ff 2010 00ff 2410 00ff 2810 00ff 2c10 ... ...$...(...,
0x00001030 : 00ff 3010 00ff 3410 00ff 3810 00ff 3c10 ...0...4...8...<

### FIFOs operations
Command
fifo → Perform operation on communication FIFOs

Synopsis
fifo init
fifo.<idx> init <mode>
fifo.<idx> status
fifo.<idx> clear
fifo.<idx> read
fifo.<idx> write <data>
fifo.<idx> wait <delay>
   where <idx> = fifo index (from 0 to 7)
        <mode> = 0 for fifo, 1 for mailbox
        <data> = data to write
        <delay> = delay to wait Not_Empty flag [0 = no timeout wait IRQ]

Description
The fifo command allows to execute operations on FIFOs. It is possible to set FIFOs either in FIFO mode or in Mailbox mode with the init command. It possible to perform read write operaion on FIFOs or to clear completely the FIFO. The wait sub operation allows to wait on a IRQ.

Examples
1:TscMon>fifo init 0
FIFO#0 is initialized in FIFO mode …

2:TscMon>fifo.0 status
FIFO#0 status = 0xe0000000
FIFO#0 current word counter : 0x00
FIFO#0 current SRAM write pointer : 0x00
FIFO#0 current SRAM read pointer : 0x00
FIFO#0 not empty : 0
FIFO#0 full : 0
FIFO#0 used as MailBox : 0
FIFO#0 error : 0
FIFO#0 reset : 0
FIFO#0 Read enable : 1
FIFO#0 Write enable : 1
FIFO#0 FIFO enable : 1

3:TscMon>fifo.0 write 12345678

4:TscMon>fifo.0 status
FIFO#0 status = 0xe1000101
FIFO#0 current word counter : 0x01
FIFO#0 current SRAM write pointer : 0x01
FIFO#0 current SRAM read pointer : 0x00
FIFO#0 not empty : 1
FIFO#0 full : 0
FIFO#0 used as MailBox : 0
FIFO#0 error : 0
FIFO#0 reset : 0
FIFO#0 Read enable : 1
FIFO#0 Write enable : 1
FIFO#0 FIFO enable : 1

5:TscMon>fifo.0 read
FIFO#0 data = 12345678

6:TscMon>fifo.0 status
FIFO#0 status = 0xe0010100
FIFO#0 current word counter : 0x00
FIFO#0 current SRAM write pointer : 0x01
FIFO#0 current SRAM read pointer : 0x01
FIFO#0 not empty : 0
FIFO#0 full : 0
FIFO#0 used as MailBox : 0
FIFO#0 error : 0
FIFO#0 reset : 0
FIFO#0 Read enable : 1
FIFO#0 Write enable : 1
FIFO#0 FIFO enable : 1

### Fill Address Range in Kernel Buffer
Command
fm → fill an address range in kernel buffer with a data set

Synopsis
fm.<ds>[<swap>] <start>[..<end>] <data>

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start offset in hexadecimal
        <end> = end offset in hexadecimal
        <data> = data set

Description
The fs command shall be used to fill a range of address in the kernel allocated buffer with a data set.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character is optional and shall be s if byte swapping is required (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets (relative to the kernel buffer base address) whose content shall be initialized according to the data size chosen.
The second parameters defines the data set to be used to fill the address range.

Examples
4:TscMon>fm.w 0..10000 w:ffffffff..1
5:TscMon>dm.w 0..40
0x00000000 : fffffffe fffffffd fffffffb fffffff7 ................
0x00000010 : ffffffef ffffffdf ffffffbf ffffff7f ................
0x00000020 : fffffeff fffffdff fffffbff fffff7ff ................
0x00000030 : ffffefff ffffdfff ffffbfff ffff7fff ................

### Fill PCI tree addresses with data
Command
fp → fill PCI tree addresses with data

Synopsis
fp.<ds>[<swap>] <start>[..<end>] data
fp1.<ds>[<swap>] <start>[..<end>] data
fp2.<ds>[<swap>] <start>[..<end>] data

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start offset in hexadecimal
        <end> = end offset in hexadecimal
        <data> = data set

Description
The fp command shall be used to fill a range of address in PCI tree.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character is optional and shall be s if byte swapping is required (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets (relative to the shared memory base address) whose content shall be initialized according to the data size chosen.
The second parameters defines the data set to be used to fill the address range.

### Fill Address Range in Shared memory
Command
fs → fill an address range in shared memory (1 or 2) with a data set

Synopsis
fs.<ds>[<swap>] <start>[..<end>] data
fs1.<ds>[<swap>] <start>[..<end>] data
fs2.<ds>[<swap>] <start>[..<end>] data

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start offset in hexadecimal
        <end> = end offset in hexadecimal
        <data> = data set

Description
The fs command shall be used to fill a range of address in shared memory with a data set.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character is optional and shall be s if byte swapping is required (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets (relative to the shared memory base address) whose content shall be initialized according to the data size chosen. TscMon creates dynamically the address mapping in order to access the shared memory.
The second parameters defines the data set to be used to fill the address range.

Examples
6:TscMon>fs.s 1000..2000 s:0..2
7:TscMon>ds.s 1000
0x00001000 : 0000 0002 0004 0006 0008 000a 000c 000e ................
0x00001010 : 0010 0012 0014 0016 0018 001a 001c 001e ................
0x00001020 : 0020 0022 0024 0026 0028 002a 002c 002e . .".$.&.(.*.,..
0x00001030 : 0030 0032 0034 0036 0038 003a 003c 003e .0.2.4.6.8.:.<.>

### Fill USR space with data
Command
fu → fill USR space with data

Synopsis
fu.<ds>[<swap>] <start>[..<end>] data
fu1.<ds>[<swap>] <start>[..<end>] data
fu2.<ds>[<swap>] <start>[..<end>] data

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <start> = start offset in hexadecimal
        <end> = end offset in hexadecimal
        <data> = data set

Description
The fu command shall be used to fill a range of address in USR space.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character is optional and shall be s if byte swapping is required (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets (relative to the shared memory base address) whose content shall be initialized according to the data size chosen. TscMon creates dynamically the address mapping in order to access the USR space.
The second parameters defines the data set to be used to fill the address range.

Examples
6:TscMon>fu1.s 1000..2000 s:0..2
7:TscMon>du1.s 1000
0x00001000 : 0000 0002 0004 0006 0008 000a 000c 000e ................
0x00001010 : 0010 0012 0014 0016 0018 001a 001c 001e ................
0x00001020 : 0020 0022 0024 0026 0028 002a 002c 002e . .".$.&.(.*.,..
0x00001030 : 0030 0032 0034 0036 0038 003a 003c 003e .0.2.4.6.8.:.<.>

### Display history of commands
Command
his → Display history of commands

Synopsis
his
Display history of commands
Commands in history list can re-executed by entering '!' followed by history line number

Description
The his (history) command allows to review the history command typed in the TscMon application.

Examples
70:TscMon>his
   0 conf
   1 conf ddr
   2 conf show ddr

### Perform i2c command
Command
i2c → perform i2c command

Synopsis
Perform i2c command
   i2c <dev> read <reg>
   i2c <dev> write <reg> <data>
   where <dev> = lm95255
        ds1339
        max5970
        bmr463_0
        bmr463_1
        bmr463_2
        bmr463_3
        pes32nt

Description
The i2c command allows to read or write to a specific i2c device by choosing the specifi offster to write or to read.

Examples
6:TscMon>i2c lm95255 read 0
i2c read: 4c 0
data = 10544681

### TSC kernel buffer operations
Command
   kbuf → TSC kernel buffer operations

Synopsis
kbuf.<id> alloc <size>
kbuf.<id> show
kbuf.<id> free
kbuf.<id> map <map> [<offset>]
kbuf.<id> unmap
   where <id> = buffer identifier [0->7]
        <size> = buffer size
        <offset> = requested address offset (optional) in hexadecimal

Description
The kbuf command allows to execute different operation on kernel buffer. 8 kernel buffer ares available. The size parameter allows to specify the size of the buffer and the parameter show list all buffers present in the system. Free parameter release the buffer

Examples
71:TscMon>kbuf show
+---+----------+----------+
|idx| b_addr | size |
+---+----------+----------+
| 0 | 77b00000 | 00100000 |
+---+----------+----------+
72:TscMon>kbuf.1 alloc 10000
Size requested: 10000
73:TscMon>kbuf show
+---+----------+----------+
|idx| b_addr | size |
+---+----------+----------+
| 0 | 77b00000 | 00100000 |
| 1 | 73d00000 | 00010000 |
+---+----------+----------+

### Read/write LMK04803 registers
Command
lmk → Read/write LMK04803 registers

Synopsis
lmk.<x> read <reg>
lmk.<x> write <reg> <data>
   where <x> = LMK index
        <reg> = register address
        <data> = data to be written

Description
Read and write LMK04803 registers. The first paramter is the index of the device. Secondly and the third parameters are the number of the register and the data to write.

Examples
1:TscMon>lmk.0 read 4
LMK0 reg:04 = 00000320

### Read/write loop from/to PCI addresses
Command
lp1, lp2 → Read/write loop from/to PCI addresses

Synopsis
lp<i>.<ds> <offset> <data> [l:<loop>]
   where <i> = 1, 2 [PCI tree index]
        <ds> = b, s, w, l [data size 1, 2, 4, 8]
        <offset> = PCI address offset in hexadecimal
        <data> = data in hexadecimal [write cycle]
        <loop> = loop count (0 -> infinite)
        If s is appended to <ds>, byte swapping if performed

Description
The lp command shall be used to loop on a range of address in PCI space.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character is optional and shall be s if byte swapping is required (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets (relative to the PCI space address). The second parameters defines the data set to be used to loop on the address range. The third parameter is the number of loop to do.

### Read/write loop from/to shared memory
Command
ls1, ls2 → Read/write loop from/to shared memory

Synopsis
ls<i>.<ds> <offset> <data> [l:<loop>]
   where <i> = 1, 2 [SHM index]
        <ds> = b, s, w, l [data size 1, 2, 4, 8]
        <offset> = Shared memory address offset in hexadecimal
        <data> = data in hexadecimal [write cycle]
        <loop> = loop count (0 -> infinite)
        If s is appended to <ds>, byte swapping if performed

Description
The ls command shall be used to loop on a range of address in shared memory space. The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character is optional and shall be s if byte swapping is required (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets (relative to the shared memory space address). The second parameters defines the data set to be used to loop on the address range. The third parameter is the number of loop to do.

Examples
63:TscMon>ls1.w 100000 12345678 l:10
device: 0
data = 12345678

### Read/write loop from/to user area
Command
lu1, lu2 → Read/write loop from/to USR addresses

Synopsis
lu<i>.<ds> <offset> <data> [l:<loop>]
   where <i> = 1, 2 [USR index]
        <ds> = b, s, w, l [data size 1, 2, 4, 8]
        <offset> = USR offset in hexadecimal
        <data> = data in hexadecimal [write cycle]
        <loop> = loop count (0 -> infinite)
        If s is appended to <ds>, byte swapping if performed

Description
The lu command shall be used to loop on a range of address in USR space.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character is optional and shall be s if byte swapping is required (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be a range of address offsets (relative to the USR space address). The second parameters defines the data set to be used to loop on the address range. The third parameter is the number of loop to do.

Examples
66:TscMon>lu1.w 100000 12345678 l:10
device: 0
data = 12345678

### Mapping operation
Command
map show → show address mapping

Synopsis
map show [<map>]
map clear <map>
   where <map> = map identifier

Description
The map command shall be used to handle the TSC address mapping tables.
The show operation displays the TSC current mapping information for the table identified by the <map identifier> parameter:
  mas_mem → mapping in PCI MEM space
  mas_pmem → mapping in PCI PMEM space

If no map identifier is given, all maps are shown.
The clear operation resets all pages in the translation table identified by the <map identifier> parameter. This destroy all mapping previously performed by any application and should be used only as a last resort operation.

Examples

92:TscMon>map show

+=========================================================+
+ Map Name : mas_mem
+ Map Size : 2048*64 KBytes
+ Win Base : 0xc40000000
+ Win Size : 0x08000000 [2048 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 01 | 01 | 00020000 | 0000000000000000 | 2003 | SHM1
| 00020000 | 01 | 01 | 00020000 | 0000000000000000 | 3003 | SHM2
| 00040000 | 01 | 01 | 00010000 | 0000000000010000 | 2003 | SHM1
| 00050000 | 00 | 00 | 07fb0000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

+=========================================================+
+ Map Name : mas_pmem
+ Map Size : 128*4 MBytes
+ Win Base : 0xc60000000
+ Win Size : 0x20000000 [128 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 00 | 00 | 20000000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

Command
map alloc → create a new entry in a map

Synopsis
map.<space> alloc <map> <addr> <size> [<offset>]
map free <map> offset
   where <map> = map identifier
        <space> = p, s, u -> remote space ( PCI, SHM or USER)
        <addr> = remote address in hexadecimal
        <size> = requested mapping size
        <offset> = requested address offset (optional)

Description

The map alloc operation creates new pages in the translation table identified by the <map> parameter:
  mas_mem → mapping in PCI MEM space
  mas_pmem → mapping in PCI PMEM space
It takes <rem_addr>, <size> and <mode> as additional parameters. If <offset> parameter is given, the driver will try to map the page at that offset otherwise dynamic allocation is performed.
The free operation delete existing pages in the translation table identified by the <map> parameter. It takes as parameter the page offset returned by the alloc operation

Examples

4:TscMon>map.s alloc mas_mem 1000 1000 0
Allocating mapping...
mapping mode: 0
5:TscMon>map show

+=========================================================+
+ Map Name : mas_mem
+ Map Size : 2048*64 KBytes
+ Win Base : 0xc40000000
+ Win Size : 0x08000000 [2048 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 01 | 01 | 00020000 | 0000000000000000 | 2003 | SHM1
| 00020000 | 01 | 01 | 00020000 | 0000000000000000 | 3003 | SHM2
| 00040000 | 01 | 01 | 00010000 | 0000000000000000 | 2003 | SHM1
| 00050000 | 01 | 01 | 00010000 | 0000000000000000 | 2003 | SHM1
| 00060000 | 00 | 00 | 07fa0000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

6:TscMon>map free mas_mem 1
Freeing mapping...
7:TscMon>map show

+=========================================================+
+ Map Name : mas_mem
+ Map Size : 2048*64 KBytes
+ Win Base : 0xc40000000
+ Win Size : 0x08000000 [2048 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 00 | 00 | 00020000 | 0000000000000000 | 0000 | FREE
| 00020000 | 01 | 01 | 00020000 | 0000000000000000 | 3003 | SHM2
| 00040000 | 01 | 01 | 00010000 | 0000000000000000 | 2003 | SHM1
| 00050000 | 01 | 01 | 00010000 | 0000000000000000 | 2003 | SHM1
| 00060000 | 00 | 00 | 07fa0000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

### MTCA.4 PON mailbox operations
Command
mbox → MTCA.4 PON mailbox operations

Synopsis
mbox read <address> [<count>]
mbox write <address> <value>
mbox info

Description
This command performs communication with the PON device voer mailbox process. It allow to read and write and to acquire firmware information and various sensor values.

Examples
21:TscMon>mbox info
Firmware revision: 3.0
AMC slot number: 3
Board name: IFC_1410
Board revision: pcb_1601.2
Board serial number: 174500053
Product name: IFC_1410
Product revision: 1410
Product serial number: 0000
Sensor TCPU:
  status = (3) valid
  value = 39
  timestamp = 2922
Sensor TPCBBOT:
  status = (3) valid
  value = 37
  timestamp = 2921
Sensor TPCBTOP:
  status = (3) valid
  value = 38
  timestamp = 2920
Sensor UPTIME:
  status = (3) valid
  value = 0
  timestamp = 2927

### Patch TSC PCI CFG register
Command
pc → read/write data from/to TSC PCI configuration space

Synopsis
pc <reg> [<data>]

   where <reg> = register offset in hexadecimal
        <data> = data in hexadecimal [write cycle]

Description
The pc command shall be used to perform PCI configuration cycles targeted to the TSC FPGA PCIe End Point. It takes up to 2 parameters.
The first parameter shall be the address offset of the configuration register to be accessed.
The second parameter shall be the data to write in the register. If it is missing, TscMon performs a read cycle on the register, displays the data and prompt for a new data to overwrite the register. To return to the command interpreter enter the “.” character. If you enter CR (Carriage Return), TscMon will read the register at <reg>+<ds> and display it current value.

Examples
17:TscMon>pc 0
  0x0000 : 10017357 [0001'0000'0000'0001'0111'0011'0101'0111] ->

### Read/write data from/to TSC IFC PON register
Command
pi → read/write data from/to TSC IFC PON register

Synopsis
pi <reg> [<data>]

   where <reg> = register offset in hexadecimal
        <data> = data in hexadecimal [write cycle]

Description
The pi command shall be used to perform read/write from/to TSC IFC PON register. It takes up to 2 parameters.
The first parameter shall be the address offset of the configuration register to be accessed.
The second parameter shall be the data to write in the register. If it is missing, TscMon performs a read cycle on the register, displays the data and prompt for a new data to overwrite the register. To return to the command interpreter enter the “.” character. If you enter CR (Carriage Return), TscMon will read the register at <reg>+<ds> and display it current value.

Examples
44:TscMon>pi 0
0x0000 : 73571410 [0111'0011'0101'0111'0001'0100'0001'0000] ->

### Patch an address in system memory
Command
pm → read/write data from/to kernel buffer allocated by TscMon

Synopsis
pm.<ds>[<swap>] <addr> [<data>]

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <addr> = resource internal address in hexadecimal
        <data> = data in hexadecimal [write cycle]

Description
The pm command shall be used to perform cycles to access the host system memory. It takes up to 2 parameters.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
The second character (optional) shall be s if the data are to be byte swapped before being written or displayed (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be address offset in th kernel buffer.
The second parameter shall be the data to write in the kernel buffer. If it is missing or equal to '?', TscMon performs a read cycle on the register, displays the data and prompt for a new data to overwrite the register. To return to the command interpreter enter the “.” character. If you enter CR (Carriage Return), TscMon will read the kernel buffer at <addr>+<ds> and display it.

Examples
21:TscMon>pm.w 0
0x00000000 : 00000000 -> 12345678
0x00000004 : 00000000 -> .
22:TscMon>pm.w 0 .
0x00000000 : 0x12345678 ->

### Read/write data from/to PCI tree address
Command
pp → read/write data from/to PCI tree address

Synopsis
pp.<ds> <offset> [<data>]
pp1.<ds> <offset> [<data>]
pp2.<ds> <offset> [<data>]
   where <ds> = b,s,w,l -> data size: 1,2,4,8
        <swap> = s if swapping is required
        <offset> = address offset in hexadecimal
        <data> = data in hexadecimal [write cycle]

Description
The pp command shall be used to perform cycles to access the PCI tree address. It takes up to 2 parameters.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
The second character (optional) shall be s if the data are to be byte swapped before being written or displayed (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be address offset in th kernel PCI tree address.
The second parameter shall be the data to write. If it is missing or equal to '?', TscMon performs a read cycle on the register, displays the data and prompt for a new data to overwrite the register. To return to the command interpreter enter the “.” character. If you enter CR (Carriage Return), TscMon will read the kernel buffer at <addr>+<ds> and display it.

### Patch TSC CSR Register
Command
pr → read/write data from/to TSC CSR space

Synopsis
pr <reg> [<data>]

   where <reg> = register offset in hexadecimal
        <data> = data in hexadecimal [write cycle]

Description
The pr command shall be used to perform read/write cycles targeted to TSC CSR registers. It takes up to 2 parameters.
The first parameter shall be the address offset of the CSR register to be accessed.
The second parameter shall be the data to write in the register. If it is missing, TscMon performs a read cycle on the register, displays the data and prompt for a new data to overwrite the register. To return to the command interpreter enter the “.” character. If you enter CR (Carriage Return), TscMon will read the register at <reg>+<ds> and display it current value.

Examples
207:TscMon>pr.w 20
0x0020 : d0990014 [1101'0000'1001'1001'0000'0000'0001'0100] ->

### Patch an Address in Shared Memory
Command
ps → read/write data from/to TSC Shared Memory

Synopsis
ps.<ds>[<swap>] <addr> [<data>]

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <addr> = SHM address offset in hexadecimal
        <data> = data in hexadecimal [write cycle]

Description
The ps command shall be used to perform cycles to access the TSC Shared Memory. It takes up to 2 parameters.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character (optional) shall be s if the data are to be byte swapped before being written or displayed (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be the SHM address offset.
The second parameter shall be the data to write in the SHM address. If it is missing or equal to '?', TscMon performs a read cycle on the SHM address, displays the data and prompt for a new data to overwrite the SHM address. To return to the command interpreter enter the “.” character. If you enter CR (Carriage Return), TscMon will read the address at <addr>+<ds> and display its content.

Examples
28:TscMon>ps.w 100000
0x00100000 : f0100000 -> 12345678
0x00100004 : f0100004 -> -
0x00100000 : 12345678 -> aabbccdd
0x00100004 : f0100004 -> .
29:TscMon>ps.w 100000 .
0x00100000 : 0xaabbccdd ->
30:TscMon>

### Read/write data from/to FPGA USR space
Command
pu → read/write data from/to FPGA USR

Synopsis
pu.<ds>[<swap>] <addr> [<data>]
pu1.<ds>[<swap>] <addr> [<data>]
pu2.<ds>[<swap>] <addr> [<data>]

   where <ds> = b,s,w,l (data size 1,2,4,8)
        <swap> = s if swapping is required
        <addr> = SHM address offset in hexadecimal
        <data> = data in hexadecimal [write cycle]

Description
The pu command shall be used to perform cycles to access the FPGA user. It takes up to 2 parameters.
The command extensions is made of 1 or 2 characters. The first character can be:
  b → for byte access
  s → for 16 bit access
  w → for 32 bit access
  l → for 64 bit access
The second character (optional) shall be s if the data are to be byte swapped before being written or displayed (meaningful only for 16, 32 and 64 bits accesses).
The first parameter shall be the USR address offset.
The second parameter shall be the data to write . If it is missing or equal to '?', TscMon performs a read cycle on the SHM address, displays the data and prompt for a new data to overwrite the USR address. To return to the command interpreter enter the “.” character. If you enter CR (Carriage Return), TscMon will read the address at <addr>+<ds> and display its content.

Examples
28:TscMon>pu.w 100000
0x00100000 : f0100000 -> 12345678
0x00100004 : f0100004 -> -
0x00100000 : 12345678 -> aabbccdd
0x00100004 : f0100004 -> .
29:TscMon>pu.w 100000 .
0x00100000 : 0xaabbccdd ->

### MTCA.4 RTM operations
Command
rtm → MTCA.4 RTM operations

Synopsis
rtm led <led_name> <led_state>
   where <led_name> = green, red
        <led_state> = on, off, slow_blink, fast_blink

Description
This command allow to control LED by chosing the color and the state.

### Semaphores operations
Command
semaphore → perform semaphore operations

Synopsis
semaphore status
semaphore get <idx> <tag>
semaphore release <idx>
   where <idx> = Index of the semaphore from 0 to 0xF
        <tag> = Unique tag [7 bits]

Description
The semaphore command allow to acquire status of the 16 semaphores. This command allows too to get and to release a specific semaphore. Use a tag to identify the semaphore.

Examples
7:TscMon>semaphore status
SEMAPHORE global status = 0x00000000
SEMAPHORE#0 : 0

8:TscMon>semaphore get 0 1234
Semaphore acquired !

9:TscMon>semaphore status
SEMAPHORE global status = 0x00000000
SEMAPHORE#0 : 1

10:AltMon>semaphore release 0
SEMAPHORE#0 released

11:AltMon>semaphore status
SEMAPHORE global status = 0x00000000
SEMAPHORE#0 : 0

### Select central or io device
Command
set → Select CENTRAL or IO device

Synopsis
set device <device>
   where <device> = central or io

Description
This command allows to select and to control CENTRAL device or IO device (only on board with both devices available). In the same TscMon application it is possible to drive both devices in a same instance of the program.

Examples
48:TscMon>set device central
   -> Device : central - OK

### Perform specific command on SMEM DDR memory
Command
smem → Perform specific command on SMEM DDR memory

Synopsis
smem ddr calib <MEM>
   where smem ddr calib <MEM> = SMEM DDR memory IDELAY alignment
        where <MEM> = Select the specific SMEM DDR3 1 or 2 or both 12

Description
This command allows to calibrate DDR memory (SMEM1 and SMEM2). The output provides a detailed view of the calibration of each DDR3 lanes. A “Y” is present when the data (write/read) is OK for a specific delay value, a “N” when the test doesn't pass. The process runs through all lanes and find the best value (delay) for each lane..

Examples
15:TscMon>smem ddr calib 1
Calibration of the SMEM1
   FPGA System Monitoring
      Temperature : 6.89 [44.30 - 5.91]
      VCCint : 0.93 [0.93 - 0.93]
      VCCaux : 1.78 [1.79 - 1.78]

Calibration pattern : 0101 1001 0011 0100 1011 0101 1001 0011
Default INC : 4
Default CNT : 0

+-------------------------------------------------------------------------------------------------------------------------------------------------
 Default delay : *
 Delay value : 00 01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39 40 41 42
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[08] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N
 Final delay 0x32: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[09] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N
 Final delay 0x32: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[10] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N
 Final delay 0x34: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[11] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N
 Final delay 0x32: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[12] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N
 Final delay 0x38: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[13] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N
 Final delay 0x3e: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[14] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N
 Final delay 0x36: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[15] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N
 Final delay 0x38: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[00] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N N N
 Final delay 0x2c: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[01] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N
 Final delay 0x30: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[02] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N N N N N
 Final delay 0x28: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[03] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N
 Final delay 0x30: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[04] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N N N
 Final delay 0x2c: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[05] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N N
 Final delay 0x2e: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[06] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N N N N N
 Final delay 0x28: *
+-------------------------------------------------------------------------------------------------------------------------------------------------
 DQ[07] test : Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y Y N N N N N N N N N N N N N N N N N N N N N N
 Final delay 0x2c: *
+-------------------------------------------------------------------------------------------------------------------------------------------------

Calibration done !
Best case is 31 for DQ[13]
Worst case is 20 for DQ[2]

### Perform DMA operation using channel <x>
Command
dma → Perform DMA operation using channel <x>

Synopsis
dma.<x> start <des_start>:<des_space>[.s] <src_start>:<src_space>[.s] <size>
dma.<x> status
dma.<x> alloc
dma.<x> free
dma.<x> clear
     where <x> = DMA channel (0 to 3)
        <space> = 0 -> PCIe bus address
        2 -> Shared Memory #1
        3 -> Shared Memory #2
        4 -> FPGA user area #1
        5 -> FPGA user area #2
        8 -> Test buffer allocated in system memory
        If .s is appended to <space>, byte swapping if performed

Description
The dma command transfers data from a source to a destination. Source and destination space can be choosen between aboved listed space. Parameters ar in hexadecimal representation. The status option provide detailed status of the last dma transfer. It is also possible to alloc / clear a specific channel for specific operation.

Examples
38:TscMon>dma.0 start 100000:2 0:8 1000
OK -> status = 2400011

### Launch test suite
Command
tinit → launch test suite

Synopsis
tinit.<x> [<testfile>] [<console>]
   where <x> = test program index
        <testfile> = path of test program to be launched
        <console> = device to be used for output messages

Description
The tinit command allows to launch the test application in a xterm or in a pseudo terminal session. <testfile> is the name of the test application to be launched and <console> the name of the serial device to be used for message output. By default, <testfile> is set to “./TscTst” and console is “/dev/pts/0”.

Examples
1:TscMon>tinit
TscTst-> Launching: ./TscTst-> Done:./TscTst 1648

### Kill test suite
Command
tkill → kill test suite

Synopsis
Kill test suite

Description
Tkill command allows to kill and to close the test environment suite.

Examples
41:TscMon>tkill

### Display a list of existing test
Command
tlist → display a list of existing test

Synopsis
display a list of existing test

Description
The command tlist simply list all test available in the test environment suite.

Examples
64:TscMon>tlist
TscTst->Command:tlist
Tst:01 [NEX] -> Get board configuration
Tst:02 [NEX] -> Calibrate SMEM1 & SMEM2
Tst:03 [NEX] -> Read/Write SMEM1 MEM
Tst:04 [NEX] -> Read/Write SMEM1 PMEM
Tst:05 [NEX] -> Read/Write SMEM2 MEM
Tst:06 [NEX] -> Read/Write SMEM2 PMEM
Tst:07 [NEX] -> Read/Write KBUF0
Tst:20 [NEX] -> DMA from KBUF0 to SMEM1
Tst:21 [NEX] -> DMA from KBUF0 to SMEM2
Tst:22 [NEX] -> DMA from SMEM1 to KBUF0
Tst:23 [NEX] -> DMA from SMEM2 to KBUF0
Tst:50 [NEX] -> Test FMC#1 & FMC#2 on IFC14xx boards

### Show status of test suite
Command
tstatus → show status of test suite

Synopsis
show status of test suite

Description
Tstatus command allows to show the current status of the test suite environment. It can be running if a test is running, idle if the test suite doesn't execute any test.

Examples
88:TscMon>tstatus
TscTST -> IDLE

### Start execution of a test or a chain of tests
Command
tstart → start execution of a test or a chain of tests

Synopsis
Start execution of a test or a chain of tests
tstart <test>
tstart <start>..<end>

Description
Tstart command allows to start one or several tests. If a range of test is selected, all tests will be executed.

Examples
121:TscMon>tstart 1
TscTst->Starting test 1..1

Tst:01->Entering:Fri Nov 17 10:51:23 2017
Tst:01->Checking tsc_central configuration
        Driver = 1.40 -> OK
        Library = 1.30 -> OK
        Vendor = 7357 -> OK
        Device = 1001 -> OK
FPGA idenfitiers
FPGA eFUSE : 0x00000000
FPGA Signature : 0x08111701
FPGA Version : 0x00010101
TOSCA Signature : 0x20160401

Tst:01->Exiting:Fri Nov 17 10:51:23 2017

140:TscMon>tstart 3..4
TscTst->Command:tstart 3..4
TscTst->Starting test 3..4
Tst:03->Entering:Fri Nov 17 10:52:18 2017

Tst:03->Executing Read / Write SHM1 MEM
Tst:03->Executing: iteration:4094 size:06078 offset:01078 -> OK
Tst:03->Exiting :Fri Nov 17 10:53:00 2017
Tst:04->Entering:Fri Nov 17 10:53:00 2017

Tst:04->Executing Read / Write SHM1 PMEM
Tst:04->Executing: iteration:4094 size:06078 offset:01078 -> OK
Tst:04->Exiting :Fri Nov 17 10:53:42 2017

### Stop current test execution
Command
tstop → stop current test execution

Synopsis
stop current test execution

Description
This command allows to stop the current test execution.

Examples
172:TscMon>tstart 3
173:TscMon>tstop

### Set test control parameter
Command
tset → set test control parameter

Synopsis
tset exec=fast -> execute test in fast mode [default]
tset exec=val -> execute test in validation mode
tset err=halt -> stop test execution if error
tset err=cont -> go for next test if error
tset loop=<n>
     where <n> = number of time a test is execute (0->infinite)
tset logfile=<filename>
tset log=<op>
     where <op> = off -> close logfile if currently open
        new -> create new logfile
        add -> append to existing logfile or create logfile

Description
The tset command allows to log test messages in a file. The logfile parameter shall be set to the file name and the log parameter shall be set to new to create the file. It is also possible to execute several time a test ot to set the condition of the test suite depending the error found.
Examples
11:TscMon>tset logfile=myLog.log
12:TscMon>tset log=new
13:TscMon>tstart 1

### Perform read/write test in PCI tree address space
Command
tp → Perform read/write test in PCI tree address space

Synopsis
tp.<ds> <start>..<end> <data> [<loop>]
tp1.<ds> <start>..<end> <data> [<loop>]
tp2.<ds> <start>..<end> <data> [<loop>]
   where <ds> = b, s, w, l [data size 1, 2, 4, 8]
        <start> = address offset in hexadecimal of first location
        <end> = address offset in hexadecimal of last location
        <data> = data in hexadecimal
        <loop> = number of loop

Description
This command allows to test a memory range by writing and reading data during a defined number of loop. It allows to define a memory range and a data. If the parameter loop is set to '0', the test executes an infinity of loop. It exit on error or when the number of loop is finised.

### Perform read/write test on shared memory
Command
ts → Perform read/write test on shared memory

Synopsis
ts.<ds> <start>..<end> <data> [<loop>]
ts1.<ds> <start>..<end> <data> [<loop>]
ts2.<ds> <start>..<end> <data> [<loop>]
   where <ds> = b, s, w, l [data size 1, 2, 4, 8]
        <start> = address offset in hexadecimal of first location
        <end> = address offset in hexadecimal of last location
        <data> = data in hexadecimal
        <loop> = number of loop

Description
This command allows to test a memory range by writing and reading data during a defined number of loop. It allows to define a memory range and a data. If the parameter loop is set to '0', the test executes an infinity of loop. It exit on error or when the number of loop is finised.

Examples
77:TscMon>ts1.w 100000..200000 r:2 l:5
device: 0
Enter any key to stop memory test
Loop [5]: 5 - 00100000 elapsed time = 2 sec

### Perform read/write test on FPGA USR memory
Command
tu → Perform read/write test on FPGA USR memory

Synopsis
tu.<ds> <start>..<end> <data> [<loop>]
tu1.<ds> <start>..<end> <data> [<loop>]
tu2.<ds> <start>..<end> <data> [<loop>]
   where <ds> = b, s, w, l [data size 1, 2, 4, 8]
        <start> = address offset in hexadecimal of first location
        <end> = address offset in hexadecimal of last location
        <data> = data in hexadecimal
        <loop> = number of loop

Description
This command allows to test a memory range by writing and reading data during a defined number of loop. It allows to define a memory range and a data. If the parameter loop is set to '0', the test executes an infinity of loop. It exit on error or when the number of loop is finised.

Examples
85:TscMon>t21.w 100000..200000 r:1 l:5
device: 0
Enter any key to stop memory test
Loop [5]: 5 - 00100000 elapsed time = 2 sec

### Wait for test to complete
Command
twait → wait for test to complete

Synopsis
wait [<tmo>]
   where <tmo> = timeout in sec

Description
This command allows to wait a delay in second the end of a test.

Examples
2:TscMon>tstart 3
3:TscMon>twait 3
Waiting for test to complete -> Tst: 03 -> DONE:OK

## Script execution
TscMon supports script execution. A script is an ASCII file containing a sequence of TscMon commands to be executed. Comments can be inserted in the script file with the character '#'. When this character is encountered by the script interpreter, it stops decoding the command line, executes it and jump to the next command.
In addition to TscMon command, the script interpreter recognize a set of operations identified by a string starting with the '$' character.
When TscMon command are executed a global error status is updated. The script interpreter has the possibility of checking that status and exiting in case of error. This allows to stop script execution if something is going wrong.
### Executing an TscMon script
The file ASCII “myscript.xfs” contains a simple script to be executed bx TscMon
#
# This is a TscMon script
#
map show # show mapping
ds.w 10000 # display content of SHM from offset 0x10000
#

To execute the script from TscMon just enter the filename precedeted by the character '@':

39:TscMon>@myscript.xfs
Start execution of script file myscript
39:TscMon>map show

+=========================================================+
+ Map Name : mas_mem
+ Map Size : 2048*64 KBytes
+ Win Base : 0xc40000000
+ Win Size : 0x08000000 [2048 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 01 | 01 | 00020000 | 0000000000000000 | 2003 | SHM1
| 00020000 | 01 | 01 | 00020000 | 0000000000000000 | 3003 | SHM2
| 00040000 | 01 | 01 | 00010000 | 0000000000010000 | 2003 | SHM1
| 00050000 | 00 | 00 | 07fb0000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

+=========================================================+
+ Map Name : mas_pmem
+ Map Size : 128*4 MBytes
+ Win Base : 0xc60000000
+ Win Size : 0x20000000 [128 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 00 | 00 | 20000000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

39:TscMon>ds.w 10000
device: 0
0x00010000 : 00000000 00000000 00000000 00000000 ................
0x00010010 : 00000000 00000000 00000000 00000000 ................
0x00010020 : 00000000 00000000 00000000 00000000 ................
0x00010030 : 00000000 00000000 00000000 00000000 ................

It shall be noted that a script file can include the execution of another script file:
#
# This is a TscMon script
#
conf show # show interface configuration
map show # show mapping
ds.w 10000 # display content of SHM from offset 0x10000
#
# call a sub-script
#
@dma.xfs

#
# This script performs a dma transfer from SHM to kernel buffer
#
dm.w 0
dma.0 start 0:8 100000:2 1000
dma.0 status
dm.w 0

86:TscMon>@myscript.xfs
Start execution of script file myscript
86:TscMon>conf show
   Static Options [0x0000e900]
      PCI IO size : 4 KBytes
      PCI MEM size : 128 MBytes
      PCI PMEM size : 512 MBytes
   Identifiers
      FPGA eFUSE : 0x00000000
      FPGA Signature : 0x14111701
      FPGA Version : 0x00010101
      TOSCA Signature : 0x20160401
   DDR3 configuration
      DDR3_SIZE : 4 Gbit [0x40000000]
   PCIe MSI counters
      MSI Requests : 0x00000001
      MSI Armed : 0x00000001
      MSI Acknowledge : 0x00000001
      MSI Status : 0x00000020
   Artix7 System Monitoring
      Temperature : 49.22 [49.71 - 13.78]
      VCCint : 0.93 [0.93 - 0.93]
      VCCaux : 1.78 [1.78 - 1.78]
86:TscMon>map show

+=========================================================+
+ Map Name : mas_mem
+ Map Size : 2048*64 KBytes
+ Win Base : 0xc40000000
+ Win Size : 0x08000000 [2048 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 01 | 01 | 00020000 | 0000000000000000 | 2003 | SHM1
| 00020000 | 01 | 01 | 00020000 | 0000000000000000 | 3003 | SHM2
| 00040000 | 01 | 01 | 00010000 | 0000000000010000 | 2003 | SHM1
| 00050000 | 00 | 00 | 07fb0000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

+=========================================================+
+ Map Name : mas_pmem
+ Map Size : 128*4 MBytes
+ Win Base : 0xc60000000
+ Win Size : 0x20000000 [128 pages]
+----------+----+----+----------+------------------+------+
| offset |flag| usr| size | remote address | mode |
+----------+----+----+----------+------------------+------+
| 00000000 | 00 | 00 | 20000000 | 0000000000000000 | 0000 | FREE
+----------+----+----+----------+------------------+------+

86:TscMon>ds.w 10000
device: 0
0x00010000 : 00000000 00000000 00000000 00000000 ................
0x00010010 : 00000000 00000000 00000000 00000000 ................
0x00010020 : 00000000 00000000 00000000 00000000 ................
0x00010030 : 00000000 00000000 00000000 00000000 ................
86:TscMon>@dma.xsf
Start execution of script file dma
86:TscMon>dm.w 0
device: 0
0x00000000 : 00000000 00000000 00000000 00000000 ................
0x00000010 : 00000000 00000000 00000000 00000000 ................
0x00000020 : 00000000 00000000 00000000 00000000 ................
0x00000030 : 00000000 00000000 00000000 00000000 ................
86:TscMon>dma.0 start 0:8 100000:2 1000
OK -> status = 20000111
86:TscMon>dma.0 status
DMA#0 CSR registers
RD: 8048a000: 00000010 : 00003000: 80000000
WR: 80800000: 00000000 : 00000000: 00000000
86:TscMon>dm.w 0
device: 0
0x00000000 : 00000000 00000004 00000008 0000000c ................
0x00000010 : 00000010 00000014 00000018 0000001c ................
0x00000020 : 00000020 00000024 00000028 0000002c ... ...$...(...,
0x00000030 : 00000030 00000034 00000038 0000003c ...0...4...8...<

### Script Parameters
An TscMon scripts can be launched with up to 10 parameters. These parameters are used within the script file through the $0. $1, ...$9 keywords.
When executing the script file, TscMon will replace '$0' by the first parameter, '$1' by the second parameter and so on up to '$9'.
The dma script has been modifier to be executed with sorce and destination given through the parameter mechanism:
#
# This script performs a dma transfer with parameters
#
fm.w 0..10000 0
dm.w 0
dma.0 start $0 $1 $2
dma.0 status
dm.w 0

176:TscMon>@dma.xsf 0:8 100000:2 1000
Start execution of script file dma
176:TscMon>fm.w 0..10000 0
device: 0
176:TscMon>dm.w 0
device: 0
0x00000000 : 00000000 00000000 00000000 00000000 ................
0x00000010 : 00000000 00000000 00000000 00000000 ................
0x00000020 : 00000000 00000000 00000000 00000000 ................
0x00000030 : 00000000 00000000 00000000 00000000 ................
176:TscMon>dma.0 start $0 $1 $2
OK -> status = 20000111
176:TscMon>dma.0 status
DMA#0 CSR registers
RD: 8048a000: 00000010 : 00003000: 80000000
WR: 80800000: 00000000 : 00000000: 00000000
176:TscMon>dm.w 0
device: 0
0x00000000 : 00000000 00000004 00000008 0000000c ................
0x00000010 : 00000010 00000014 00000018 0000001c ................
0x00000020 : 00000020 00000024 00000028 0000002c ... ...$...(...,
0x00000030 : 00000030 00000034 00000038 0000003c ...0...4...8...<

### Script Control Operations
In addition to TscMon command, the script interpreter supports the following control operations:
$echo	→ display a string on the TscMon console
$exit	→ force exit from TscMon
$sleep	→ wait for so many seconds
$usleep	→ wait for so many microseconds
The following script prints the message “testing timer”, start the timer, read it, wait 1 second and read it again:
#
# This script performs control operations
#
$echo testing control operations
ds.w 100000
$sleep 1
dm.w 0

229:TscMon>@timer.xfs
Start execution of script file timer
testing control operations
229:TscMon>ds.w 100000
device: 0
0x00100000 : 00000000 00000004 00000008 0000000c ................
0x00100010 : 00000010 00000014 00000018 0000001c ................
0x00100020 : 00000020 00000024 00000028 0000002c ... ...$...(...,
0x00100030 : 00000030 00000034 00000038 0000003c ...0...4...8...<
229:TscMon>dm.w 0
device: 0
0x00000000 : 00000000 00000004 00000008 0000000c ................
0x00000010 : 00000010 00000014 00000018 0000001c ................
0x00000020 : 00000020 00000024 00000028 0000002c ... ...$...(...,
0x00000030 : 00000030 00000034 00000038 0000003c ...0...4...8...<

### Exiting from a Script
If the 'q' command is encountered during script execution, TscMon returns to single command execution.
If the $exit operation is encountered, TscMon exits and returns to the shell.
The third way to exit from a script is when a command execution returns with a the global error flag set. The global error flag is set by the compare (cb, cc, ce, cm, cp,....) and test (tb, ts, tu) commands when a data compare error is detected.
The followin scrpt performs two data compare. The first one shall be successful and the second one shall fail. After each test a message should be printed, unless an error is detected.
#
$echo Testing cs command
ps.w 12 1234
cs.w 12 1234 ffff
$echo Test ok
cs.w 12 5678 ffff
$echo Test not ok
#

Executing the script shows that the second message is not printed because the script execution has been stopped after detection of compare error.

58:TscMon>@error.xfs
Start execution of script file error
Testing cm command
58:TscMon>ps.w 1012 1234
58:TscMon>cs.w 1012 1234 ffff
00001012 : 00001234 - 00001234 [0000ffff]
Test ok
58:TscMon>cs.w 1012 5678 ffff
00001012 : 00005678 - 00001234 [0000ffff] -> ERROR !!!

### Command Execution in Batch Mode
Command can be given as parameter when launching TscMon to be executed in “batch” mode. In this case TscMon execute the command and exit in order to return to the shell interpreter:

root@IFC1410:~/TSC/src/TscMon# ./TscMon "conf"
Size requested: 100000
kernel buffer allocated: 0xc000000077b00000 77b00000 100000
MEM Win Base : 0xc40000000
PMEM Win Base : 0xc60000000
   Static Options [0x0000e900]
      PCI IO size : 4 KBytes
      PCI MEM size : 128 MBytes
      PCI PMEM size : 512 MBytes
    PCIE identifier
      Board ID : Reserved
      Revision ID : 0
      PCIe EP : PCIe EP 1
   DDR3 configuration
      DDR3_SIZE : 4 Gbit [0x40000000]
   Identifiers
      FPGA eFUSE : 0x00000000
      FPGA Signature : 0x14111701
      FPGA Version : 0x00010101
      TOSCA Signature : 0x20160401
   PCIe MSI counters
      MSI Requests : 0x00000003
      MSI Armed : 0x00000003
      MSI Acknowledge : 0x00000003
      MSI Status : 0x00000020
   Artix7 System Monitoring
      Temperature : 49.22 [49.71 - 13.78]
      VCCint : 0.93 [0.93 - 0.93]
      VCCaux : 1.78 [1.78 - 1.78]
   Current device
      central
Freeing kernel buffer 0 : 77b00000

If the TscMon command is a script execution, the sequence of command is executed. TscMon returns to the shell only if a “$exit” operation is encountered in the script.

root@IFC1410:~/TSC/src/TscMon# ./TscMon @dma.xfs
Size requested: 100000
kernel buffer allocated: 0xc000000077b00000 77b00000 100000
MEM Win Base : 0xc40000000
PMEM Win Base : 0xc60000000
Start execution of script file dma
fm.w 0..100000 0
device: 0
dm.w 0
device: 0
0x00000000 : 00000000 00000000 00000000 00000000 ................
0x00000010 : 00000000 00000000 00000000 00000000 ................
0x00000020 : 00000000 00000000 00000000 00000000 ................
0x00000030 : 00000000 00000000 00000000 00000000 ................
dma.0 start 0:8 100000:2 1000
OK -> status = 20000111
dma.0 status
DMA#0 CSR registers
RD: 8048a000: 00000010 : 00003000: 80000000
WR: 80800000: 00000000 : 00000000: 00000000
dm.w 0
device: 0
0x00000000 : 00000000 00000004 00000008 0000000c ................
0x00000010 : 00000010 00000014 00000018 0000001c ................
0x00000020 : 00000020 00000024 00000028 0000002c ... ...$...(...,
0x00000030 : 00000030 00000034 00000038 0000003c ...0...4...8...<

        _______ __ __
        |__ __| | \/ |
        | |___ ___| \ / | ___ _ __
        | / __|/ __| |\/| |/ _ \| '_ \
        | \__ \ (__| | | | (_) | | | |
        |_|___/\___|_| |_|\___/|_| |_|

     +------------------------------------------+
     | IOxOS Technologies Copyright 2015-2017 |
     | TscMon - CENTRAL 1001 diagnostic tool |
     | Version 1.40 - Dec 4 2017 10:04:17 |
     | FPGA Built Nov 28 2017 13:32:35 |
     | FPGA Sign 08111701 |
     | Driver IFC1410 Version 1.40 |
     | ******* Official release 1.4.3 ******* |
     +------------------------------------------+

1:TscMon>